Erik D. Perry

4/23/07

NCSX Base Support Structure Fabrication – Job 1752

Preliminary fabrication estimate based on unsigned drawings received from J. Rushinski 4/12/07

304 SS W8 x 15 equivalent, 6 pcs 24’ @ $2,797 ea*					$17K

304SS W4 I-beam, 3 pcs 24’ @$1,400 ea						$  5K

304SS ¾” plate, 1 pc @ $4,233 ea*							$  5K

Weld rod and rotobores								$  3K

Subtotal materials							$30K

G&A on materials @ 25%						$  8K

Total Materials							$38K

Welder @ 4 hrs per W8 I-beam “T” weld for 36 locations		144 MH

Welder @ 2 hrs per W4 I-beam “T” weld for 12 locations		  48 MH

Metalman to cut and drill beams 					  66 MH

Total man-hours					258 MH

Total labor cost at $81/hr loaded					$21K

Total cost (loaded)				$59K

*quote from Samson Metals 4/23/07

NCSX Base Support Structure Design – Job 1752

Design Estimate

Engineering and stress analysis		2 man-months

Design						3 man-months