Relief area cut into cast wall

The above pictures illustrate how much casting wall interference there will be on the type A casting.  The current machining models for all three winding forms have this interference problem to some degree.

The models have a 3” counterbore that extends .75” from the face and the remainder of the feature is a 1.5” radius (see below).  This is why Major Tool had to perform the grinding around the counterbores on C4 in order to get the 3” diameter gage to fit.