Coil C3

Overall the layout scan of C3 was very good.  There is one area found that shows little or no stock.  The area of concern is highlighted below.  The scan shows that it could be anywhere from 3/16” below or above the nominal dimension.  This area was designed to have ½” machine stock.

# Text boxes

The green area at the very tip of the racetrack peak is the area of concern.