Conference call with EIO re:  interference reviews – August 31, 2006

NH, LS, FM, PH, DW, RS, MG, PD, CR

- A-A appear to not have any interference issues.

  - Slide 12- A casting - Dave notes that one wing area didn’t have the leader from the -/- tolerance note to the upper wing area; asked what was assumed. (dwg. 114, sheet 10)   MG will check.

- All type C interfaces appear to be good.

  - C4 pocket dimensions are mostly (-) and OK (slide 16) (this was singled out as an example of Tom’s analysis).

  - There were some areas ground at PPPL on the C castings – it appears that all C’s should be OK now.

- A-B is much more complex, with varying tolerances in areas:

- Only 3 inspection points in top pocket. (slide 6)

- Mike Griffith questioned where the +0/-.25 tolerance comes from (slide 8- see pocket )– Rev. 8.  (dwg. -114).  MTM doesn’t have Rev. 8 – only Rev. 7 posted on the web site.

  - These changes were noted in the August 10 meeting notes.

  - This area is already being machined.

  - NCSX will post the  Rev. 8 drawing today, if possible.  We will update the entire Zip file starting with this.

- B4 shows some excess stock, but appears to be OK.

- Type B, Datum A there is a lack of data points.  (slide 10, only 3 points in upper pocket).  More points will be requested here.

- Slide 10 – B1 through B6 all appear to have two “gray” areas.

  - MTK will review these areas this afternoon.

Other drawing discussions:

    - MG notes 4 drawing changes: -115, Rev. 9

      - VPI holes – no issues.

      - Tapped holes in the T – no issues.

      - Eliminating of counterbores – they’re already in on B1.  They will be deleted from B2-B6;  only a location spot will be shown.

      - Mark alignment note:  MTM will add a line perpendicular and parallel to the base of the T.

      - Reference B castings – Dave’s slides shown last week.  Corner radius was shown as ¼” Dave agrees that ½” is acceptable.  (covered under general notes already).

      - NCSX has to revise the spec to add -115, Rev. 9.

      - EIO will issue one NCR to cover the Type B pad non-conformances.

    - Update:  On 3rd setup for B1 – going well.  Overstock area will likely be on the 30’ Mitsu.

    - B2 on second side.

This area appears to be a depression on B-1

This area is currently being checked by PPPL for interference – On B-1 & B-2

This same gray area appears on B-2 thru B-6

B-5 & B-6 both have the same gray area that is causing a problem on B-1 – much smaller area