Document reviewed: D-NCSX-MCF-003

Title:  MC Fabrication- VPI Station Activities for the Twisted Racetrack Coil

Date: July 8, 2005

Attendees: Frank Terlitz, Mike hause and Buddy Kearns. Additional comments from earlier meeting are included Tom Meighan, Bill Slavin and Steve Raftopoulos

- A more stringent vacuum test of the bag mold needs to be performed prior to installing the shell, to minimize the risk of leaks developing in the autoclave.

- More technicians need to be trained on operating the viscometer.

- The epoxy digital scale was not working properly- get repaired.

- Procure 30 pound calibrated weight for calibrating scale.

- The secondary heaters on the autoclave did not work.  Get them operational.

- Need better map of the thermocouple locations.

- Add higher exit points to the autoclave to handle the upper most sprues.

- Raise the overfill tank and return manifolds higher.

- Add heaters to the main supply and return manifolds on the control panel.

- Add drains to the main manifolds.

- Add 2 more thermo readouts to the display on the platform.

- Install vacuum gauge wires- the vacuum gages at the control panel were not connected.