VV Cooling/Heating Thermohydraulic Requirements – P Goranson 2/23/06

The following are the flow parameters across the baseline braided hose on the VV during cooling and bakeout. The values are based on actual heat transfer measurements and pressure drops measured on prototype hose and mounts.

Assumptions:

Cooling is for a 15 minute cooldown with 14.4 MJ full upgrade operation.

The VV is at an elevated ratchet temperature of 48 C.

The new insulation scheme has reduced the bakeout heat input to 8.17 kW with VV at 350 C, 4.75 kW at 150 C.

192 hoses, averaging 18 feet in length.

Hose I.D. is 0.25 inches

A mounting saddle every 5 inches along the hose length.

Only half the tube perimeter is effective.

Helium Bakeout at 350 C		8.17 kW

He flow total for the VV		325 cfm at 20 atmos absolute

Pressure drop across hose		0.9 atmos

Temperature in			374 C

Temperature out			368 C

Flow velocity				25 m/s

Helium Cooling

He flow total for the VV		386 cfm at 20 atmos absolute

Pressure drop across hose		1.9 atmos

Temperature in			20 C

Temperature out			25.3 C

Flow velocity				30 m/s

Air Bakeout at 150 C		4.75 kW

Air flow total for the VV		258 cfm at 8 atmos absolute

Pressure drop across hose		1.54 atmos

Temperature in			166 C

Temperature out			160 C

Flow velocity				20 m/s