Options

- Baseline

- uniform shim every layer (must be overpacked)

- no shims, extra turn (must be overpacked)

- hard shims under cladding only

Issues

- Lateral dimension vs radial dimension

- “cutting the corners”

- uneven distribution of turns

- variable conductor dimensions - +/- .01? each turn

- how to hold pack when the vulcanizing is put on?

Paths forward

- Wind a trial on side A, measure, wind again and check for repeatability

- Finish side B, measure, then pull the shims and squeeze in a third layer?

- Finish side B with baseline shimming option, but with a slightly full shim size, measure, wind side A with no shims, push into theoretical position.  Try with last TRC casting data to figure out machined surface position.

- Finish side B with diving boards in 12 places around perimeter between turns 6 and 7, all shims the same thickness? Measure compression of turns 7-9, demonstrate no keystoning.  Try with last TRC casting data to figure out machined surface position.  Wind side A with no shims, force into position relative to casting.

- Finish side B by;

  - measure height and width of 6 layer pack

  - square up and put hard stops on side clamps

  - push laterally on specific clamps to see if height can be recovered

  - side studies to consider: think of ways to establish/enforce “square” winding pack at clamp locations, try keystone test with tamping/setting of turns

  - measure height and width again of 6 layer pack

  - shim on top of layer 6 (use some diving boards) so top of shim/ bottom of layer 7 is per Pro-E surface

  - measure layers 7, 8, 9 for info,

  - try to adjust height of layer 9 with clamps to a prescribed surface

  - tamp between clamps as finishing step

  - periodically check alignment of arm, consider adding more targets (seat type instead of ball type).

  - Figure out how to tell if turns move when vulcanizing tape is put on

In parallel with finishing side B

- Try with last TRC casting data to figure out machined surface position.

- Take whatever TRC surface data is convenient, through ground wrap, on top of cladding, remove one piece of cladding and test that area

- Finish ground wrap

- Figure out how to measure conductor dimensions as it comes off the spool

- square up and put hard stops on side clamps

Wind side B

- Flip turning wheel

- Wind side A with no shims, 10 turns

- try to adjust height of layer 10 with clamps to prescribed surface

- tamp between clamps as finishing step force into position relative to casting or to prescribed surface