# Text boxes

Heating jacket

Epoxy Mix Tank

Vac. Pump A-VP-1

Vent

P1

Epoxy Filter

C38

Heating element

NCSX Modular Coil VPI Flow Diagram

2/15/06      [Procedure D-NCSX-MCF-003]            J.H. Chrzanowski

Autoclave Parameters:

- Heating to 135 degrees C

- Max. Pressure 10 psig

- Vacuum to mTorr range

Epoxy Supply manifold

Heating element

Epoxy Supply manifold

Key

Vacuum tubing

Brass ball valve

Pressure tubing

Poly-flo tubing

High temp [Chemflor] tubing

PVC/copper tubing

Nitrogen supply from NB Boil-off

A-SV-4

Vac. Pump A-VP-2

A-VV-1

A-VV-2

Cold Trap

Epoxy Dump

D18

D9

To Autoclave

Sample

D3

D7

D4

D8

Hardener

& Accelerator

Resin

Heating jacket

Tank 2

Tank 1

Vac. pump

Vent

D2

D1

Vent

D6

Vent

D5

Tank 3

Drain valve

Drain valve

Drain valve

A-SV-5

Relief Valve (10 psi)

Cold Trap

Autoclave

Zone 2   (24) Sprues

“Zone 3”

(12) Sprues

Zone 1

(6) Sprues

Overflow Tank

TYGON tubing

N2

Side “A”

Lower Manifold

Side “B” UPPER MANIFOLD

Side “A” UPPER MANIOLD

Vent

D17

D16

D15

D10

D13

D14

D12

D11

Valve Nomenclature:

- “D” Valves: designates delivery system valves

- “A” Valves: designates Zones 1 & 2 epoxy feed valves

- “B” Valves: designates Zone 2 epoxy exit valves

- “C” valves: designates Zone 3 epoxy exit valves

- “A –C” valve numbers: designates the sprue #

- Odd numbered valves [1, 3...etc]: designates MC Side A sprues

- Even numbered valves [2, 4..etc]: designates MC Side B sprues

Sample

Sample valve

A3

A1

B9

B7

A5

A7

A9

V1

Side “B”

Lower Manifold

A10

A8

A6

B8

B10

C37

A4

C9

C10

C32

C31

Epoxy Filter

Heating element

Heating element

Regulator