PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #   5073

COGNIZANT INDIVIDUAL:	Michael Kalish

ECN TITLE:  TF Coil Wedge Structure Update

ASSOCIATED ECP:  None

CC/WP/Job:	9450 1*** 1361	     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE131-085 | 1 | TF Coil Nose Casting Machining |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Modify per attached drawing: Sheet 1- Note 2 added referring to either the weldment or casting specification dependant on method of fabrication Sheet 1 ZoneE5 and B6 - Datum A removed Sheets 1 &2 - Title changed to “Wedge Structure Detail” Sheet 2: Circled areas indicate where references to Datum A and Datum B are removed Sheet 2 Zone E11 – Note added to allow radiuses on pockets if wedge is manufactured from a weldment Sheet 2 Zone H10 - .50 inch dimension no longer reference dimension Sheet 2 Zone C12 – Note added to reference assembly drawing for final machine tolerances Sheet 2 Zone A8 – Note added to allow excess material on surface to be machined away in final assembly

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #  5073

REASON FOR CHANGE: Option added to manufacture wedge as weldment instead of casting. Option added to allow vendor to adhere wedges to assembly and machine wedge surface as final operation. Opportunity for cost savings and improved assembly technique.

ENGINEERING CHANGE PROPOSAL: DATE: 2/2/06

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESPONSIBLE LINE MANAGER: