| Research program phase/Measurement | Diagnostic technique |
| --- | --- |
| 1. Initial Operation (B=0.5 T, room temperature) |
| Ip | Rowgowski coil |
| Wide-angle image of plasma/wall | Visible camera (1) |
| 2. Initial Field Line Mapping (no plasma) |
| Vacuum flux surfaces | E-beam, fluorescent probe & CCD camera |
| 3. 1.5 MW Initial Experiments (1.5 MW NBI, B=1.2 T, cryogenics, minimal PFCs) |
| Boundary position and shape | Saddle loops, flux loops, B probes, V3FIT |
| Total stored energy | Diamagnetic loop |
| Wide-angle image of plasma/wall | Visible cameras with filters (2) |
| Core Te | Basic Thomson scattering or filtered SXR diodes, & x-ray crystal spectrometer |
| ne profile | FIR interferometer/polarimeter |
| Core Ti | X-ray crystal spectrometer |
| Total Prad | Wide angle bolometer |
| Low m,n MHD modes (<100 kHz) | Compact soft x-ray arrays (8 20-channel arrays) |
| Magnetic axis position | Compact soft x-ray arrays & 3-D EFIT |
| Impurity identification | Visible spectrometer |
| VB, H & carbon line emission | Visible filterscopes |
| PFC temperature | Compact IR camera |
| 4. 3 MW Heating (3 MW NBI, full PFCs, B=2.0 T, 350 C bake) |
| Te profile | Full Thomson scattering system |
| Ti, v profiles | DNB & CHERS |
| Rotational transform profile | DNB & MSE, FIR inter./polar., V3FIT |
| Higher m,n MHD modes | Additional soft x-ray arrays (8 20-channel arrays) |
| High-frequency MHD (<5 MHz) | High-frequency Mirnov coils |
| Flux surface topology | Tangential SXR camera |
| Impurity concentrations | Absolute VUV spectroscopy |
| Zeff profile | Thomson scattering detector system |
| Prad profile | Core bolometer array |
| Fast ion loss | Fast ion loss probe, IR camera |
| Ion energy distribution | Neutral particle analyzer |
| Neutron flux | Epithermal neutron detector |
| SOL ne and Te | Movable Langmuir probe |
| Edge neutral pressure | Fast pressure gauges |
| 5. Confinement &  push (3 MW NBI & 6 MW NBI or RF, divertor) |
| Core ne fluctuations | Fluctuation diagnostic (HIBP and/or BES) |
| Core helium density profile | DNB & He CHERS |
| Divertor Prad profile | Divertor bolometer arrays |
| Divertor plate temperature | Fast IR camera & thermocouples |
| Target Te & ne | Plate-mounted Langmuir probes |
| Divertor recycling | Divertor filtered 1-D CCD camera |
| Divertor Impurity concentrations & flows | Divertor VUV spectroscopy |
| 6. Long pulse (Existing heating & 3 MW long pulse NBI or RF) |
| Divertor Te & ne profiles | Divertor Thomson scattering |