| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 1____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation The peer review should review the drawings going to the vendor. There should be a subgroup of the participants at this meeting focused on the outstanding issues that were not (and were not organized to be) comprehensive. Originator R. J. Hawryluk Name/Organization |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) ACTION: B. Nelson to announce when the drawing package is ready, and a subgroup will be reconvened. X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 2____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation QA should participate in these reviews. Originator R. J. Hawryluk Name/Organization |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) QA to be included in the next review. X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 3____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation Need to define a way to test the integrity of the poloidal break prior to winding the coil. Originator R. J. Hawryluk Name/Organization |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) Action: Jim Chrzanowski to develop test plan. X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 4____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation The copper cladding concept needs further development to assess cost & schedule impact. Originator R. J. Hawryluk Name/Organization |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) Action: B. Nelson Bob Parsells has been assigned to evaluate concept design. X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 5____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation Document the field errors from the case with no break as well as one poloidal break. Physics to define the driving factors for the eddy currents. Originator R. J. Hawryluk Name/Organization |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) ACTION: W. Reiersen to evaluate / assign X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 6____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation What is the impact of not including a toroidal break on the 3 sections which are joined? Is the eddy current time constant & hence the eddy currents significantly larger? Originator R. J. Hawryluk Name/Organization |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) ACTION: Wayne Reiersen to evaluate / assign. 0 Concur 0 DISAGREE X OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 7____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation Is 20 msec flux penetration sufficient? Is it too expensive for the benefit? Does it eliminate the need for extensive analysis? Originator R. J. Hawryluk Name/Organization |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) ACTION: W. Reiersen to evaluate X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 8____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation Does the spatial distribution of lateral load change for different modular coil current distributions? E.g., the flexibility scenarious. Originator M. Zarnstorff Name/Organization Physics |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) ACTION: D. Williamson to have analysis performed and incorporate results into the design if needed. X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 9____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation Have casting vendor install monuments onto the castings. Ideally the monuments would be in identical locations among the similar coil forms. [Monuments could be 1/8” via holes, machined 1/8” deep.] Originator S. Raftopoulos Name/Organization PPPL/Engineering |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) ACTION: ORNL to add this feature to the drawings. Jim Chrzanwoski to provide the information to ORNL. X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |

| WP # (ENG-032) PPPL DESIGN REVIEW CHIT CHIT # 10____ |
| --- |
| COMPONENT/SUBSYSTEM/SYSTEM NCSX Winding Form, Cladding & Tolerances Peer Review Cognizant Design Engineer B. Nelson Date of Review 1-23-03 | PEER CDR PDR FDR |
| SUBJECT: (CHECK AS APPLICABLE) Requirements Hardware Safety Analysis Configuration Cost/Schedule Performance Reliability/Maintainability Quality |
| Comment/Concern/Recommendation Is there another way to “chill” coil without adding copper plates. For example, pot coil with thermal conductive epoxy. Originator L. Dudek Name/Organization PPPL/Engineering |
| REVIEW BOARD COMMENT/RECOMMENDATION (Address technical, cost, and schedule impacts as appropriate. If CHIT is not adopted, provide technical reason - do not simply state “out-of-scope or N/A” without explaining.) ACTION: Jim Crhzanowski to investigate the possible use of thermally conductive epoxy. Thermally conductive. X Concur 0 DISAGREE 0 OTHER CHAIRPERSON L.E. Dudek Date: 1-23-03 |
| Cognizant Design Engineer’s Response/Disposition: Signature Date: |
| Responsible RLM Review |
| 0 APPROVE COG DISPOSITION 0 DISAPPROVE COG DISPOSITION | Signature Date: |
| Cognizant Design Engineer Close-Out Sign when action required by disposition is complete. Signature Date: |