Report

There were 11 chits. The main issues covered by the chits were:


1.	Need further investigation of how the parts are held together during assembly. The committee did not receive enough information to be convinced that the under-wrap epoxy was effective and wanted a strapping option to receive another look. The cog needs to document his design decisions in this area. 
2.	The committee did not receive enough information to be convinced that the inner two turns would be adequately supported, and suggested that the inboard lip be extended. The cog has considered this and believes the support is adequate and extending the lip would be costly and unnecessary.  The cog will document the final decision. 
3.	The procurement plan needs to be re-visited. The committee was not convinced by the plan to delay final machining of the production castings pending results of the first coil, and suggested two alternatives. The cog needs to re-evaluate and document a plan. 
4.	The spec is appropriately modeled after the MCWF spec. Recent improvements to that spec should be considered for inclusion in the TF casting spec.
	


It should be noted that the design and design documentation were substantially complete. The cog has done a thorough job and considered extensive input from other engineers.  The consensus of the committee is that the additional work needed is to document decisions made, rather than extensive re-work of the design and analysis. We estimate 5 working days to resolve these issues and expect the package to be issued for procurement by July 31.  Thus we are comfortable concluding that the review is successful pending resolution of chits.

Charge questions, and committee response:



1.	Are the wedge casting SOW and technical specification (C-spec) complete and ready to issue? 
	

	1.	Yes, subject to revisions based on the chits, followed by sign-off and release per project procedures.
		

2.	Is the drawing package complete and ready for fabrication? 
	

	1.	Yes, subject to revisions based on the chits, followed by checking, sign-off, and release per project procedures.
		

3.	Are the wedge casting and associated TF assembly analyses complete and checked? 
	

	1.	Analyses have been completed. Out-of-plane analyses and in-plane support for middle two turns need to be reviewed off-line with Fred Dahlgren, Mike Kalish, and Len Myatt.
		

4.	Is the design for integrating the wedge castings with the TF conductor sound and practical, including electrical insulation, bonding, fixturing?
	

	1.	How the parts are held together during assembly still needs to be resolved.
		

5.	Are the tolerances of the TF coil / wedge casing assembly achievable and adequate for final machine assembly?
	

	1.	Yes.
		



Thanks,

Hutch