Design Review documentation – Results

Title:	NCSX Poloidal Field Coil Review 		WP#: 		 (ENG-032)

Type of Review:	 Peer	 CDR	 PDR	  FDR

Cog Individual:	J. Chrzanowski		Date of Review: 	2/20/08

Review Board Members:	Invited attendees :

Chairperson  A.vonHalle		F. Malinowski		A. Brooks

T. Hunter		T. Meighan		J. Makiel

C. Neumeyer		L. Sutton		D. Rej

S. Ramakrishnan		H. Neilson		M. Kalish

W. Reiersen		J. Rushinski		R. Simmons

L. Dudek		R. Parcells

F. Dahlgren		J. Harris

Regulatory Compliance  J. Levine		M. Cole

Items Reviewed:	Sat.	Unsat.	Comments

Appropriate requirements identified 			SRD in review (not yet approved)

Development plans and schedules

Regulatory compliance including USQD and NEPA			Not covered in this review

Disposition of CHITS from previous reviews

Cost objectives			tolerance budget should be established

Other review objectives addressed

(attachment 4 of ENG-033)

SUMMARY OF RESULTS:

The design of the NCSX PF4, PF5 and PF6 coils was reviewed.  Detailed aspects of the proposed coil construction were presented including all physical dimensions, and specifications for epoxy, insulating materials, and conductors (common to all three coils).  The expected mechanical and electrical performance of the completed coils was reviewed, and a summary of analysis and testing needed to develop a good fabrication plan was available.  Drawings for all three coils have been completed and were available for this review, but questions on several design details remained unanswered.

The review committee concurred that this review should be considered incomplete, and that the committee should reconvene after the final approval of the System Requirements Document, and the availability of documented (and reviewed) support analysis.

Disposition: [check one]

Acceptable

Acceptable pending resolution of concerns- CHITS identified above must be resolved prior to installation.

____X_ Incomplete - Additional design work is required prior to another design review.

Chairperson Signature: A. vonHalle________________________Date: ________________

Distribution:   Review Board Members, Operations Center, Cognizant Design Engineer, System Engineer(s), Attendees, QA, ES&H, Security