Design Review documentation – Results

Title:	NCSX Trim Field Coil Review 		WP#: 	1435	 (ENG-032)

Type of Review:	 Peer	 CDR	 PDR	  FDR

Cog Individual:	M. Kalish		Date of Review: 	3/24/08

Review Board Members:	Invited attendees :

Chairperson  A.vonHalle		H. Neilson		A. Brooks

S. Ramakrishnan		T. Meighan		J. Makiel

J. Chrzanowski		J. Rushinski		R. Simmons

F. Dahlgren		K. Ranahan		S. Raftopolous

R. Hatcher		B. Stratton		J. Harris

P. Heitzenroeder

Regulatory Compliance

Items Reviewed:	Sat.	Unsat.	Comments

Appropriate requirements identified 			GRD/SRD Updates needed (see chits)

Development plans and schedules

Regulatory compliance including USQD and NEPA			Not covered in this review

Disposition of CHITS from previous reviews			Peer review Chits

Cost objectives			Not covered in this review

Other review objectives addressed

(attachment 4 of ENG-033)

SUMMARY OF RESULTS:

The preliminary design of the NCSX trim coils was reviewed.  Preliminary drawings and a draft of the System Requirements Document (SRD) were available, and the optimization/evolution of the design vs. design objectives/margins was presented.  Material specifications (although not complete) and proposed winding schemes were reviewed in the light of system requirements.  The coil mounting structure was reviewed, but material for clamps has not yet been specified, and details for both the coil mounting and coil lead structures need to be further developed.  Preliminary stress analysis for both the coil and mounting structures was presented, which has resulted in the proposed stiffening of the coil corners, and will have to be revisited in stress analysis of the final design configuration.  Coil cooling analysis was reviewed, as well as the resolutions of chits from a previous peer review.

There were 18 chits recorded during this review, concerning system requirements and interfaces, required analysis, and proposed changes to design details.  The review committee concurred with all chits, and agreed that this review was successful pending resolution of the chits.

Disposition: [check one]

Acceptable

X	 Acceptable pending resolution of concerns- CHITS identified above must be resolved prior to installation.

____    _ Incomplete - Additional design work is required prior to another design review.

Chairperson Signature: A. vonHalle________________________Date: __3/26/08______________

Distribution:   Review Board Members, Operations Center, Cognizant Design Engineer, System Engineer(s), Attendees, QA, ES&H, Security