Major Tool & Machine, Inc.

Page: 1

1458 East 19th Street

MTM N/C: 19289

Date: 02/20/06

Indianapolis, IN 46218-4289

User ID: MCCORKLE

PRINCETON PLASMA PHYSICS LAB

Customer:

Telephone:

609-243-3655

Contact:

Mike Viola

mviola@pppl.gov

E-Mail:

609-243-3248

Fax:

S005243-F/Ln:2

Customer P.O.:

/

Part:

3

Qty:

0

Revision:

SE120-003

Drawing ID:

317-636-6433

Telephone:

DOUG MCCORKLE

Reported By:

Fax:

317-634-9420

E-Mail:

dMcCorkle@MajorTool.com

Problem:

PORT NB HAS DEFORMATION TO HOLE PATTERN AFTER WELDING HAS BEEN COMPLETED ON

PORT 4  A/B AND 12 A/B

HOLES DO NOT ALIGN TO MATING THREADED HOLE IN NB COVER. HOLES DID ALIGN AFTER NB

WAS WELDED IN,BUT DO NOT NOW THAT PORT 4 AND 12 IS COMPLETED.

Proposed Disposition:

CUSTOMER DISPOSITION REQUIRED.

THE FLANGE IS ALSO OUT OF FLAT UP TO 1/16".

UNIT # 1 HOLES WERE OPENED UP TO 5/8" DIAMETER TO PROVIDE THE NECESSARY CLEARANCE

FOR ASSEMBLY PRIOR TO VACUUM TESTING.  THE EXTRA WELDING ON UNIT # 1 WAS SUSPECTED

TO BE THE CAUSE OF THE EXCESS DISTORTION.  THIS PROVED INCORRECT AFTER UNIT # 2

FLANGE ALSO DISTORTED.  UNIT # 3 HAS NOT BEEN INSTALLED YET, BUT IS EXPECTED TO REACT

THE SAME.  MTM RECOMMENDS OPENING ALL NB FLANGE HOLES UP TO 5/8" AND RE-FACING THE

FLANGE FLAT AFTER ALL PORTS ARE WELDED IN PLACE (A MINIMUM THICKNESS WILL BE

NEEDED).

0

Number of additional pages:

Customer Disposition:       [   ] Use As Is          [  ] Rework          [  ] Repair          [  ] Scrap          [  ] Replace

Date:

Title:

Technical Contact Approval:

Date:

Title:

Buyer Approval:

Title:

Date:

Major Tool Implemented By:

/Open

n:\mtmapps\Mtnonc14.qrp

Major Tool and Machine, Inc.  1458 East 19th Street, Indianapolis, IN 46218-4289  Tel: 317-636-6433  Fax: 317-634-9420

Nonconformance Report: Major Tool NC19289

This is for SE120-003

Problem:

PORT NB HAS DEFORMATION TO HOLE PATTERN AFTER WELDING HAS BEEN COMPLETED ON

PORT 4  A/B AND 12 A/B

HOLES DO NOT ALIGN TO MATING THREADED HOLE IN NB COVER. HOLES DID ALIGN AFTER NB

WAS WELDED IN,BUT DO NOT NOW THAT PORT 4 AND 12 IS COMPLETED.

THE FLANGE IS ALSO OUT OF FLAT UP TO 1/16".

UNIT # 1 HOLES WERE OPENED UP TO 5/8" DIAMETER TO PROVIDE THE NECESSARY CLEARANCE

FOR ASSEMBLY PRIOR TO VACUUM TESTING.  THE EXTRA WELDING ON UNIT # 1 WAS SUSPECTED

TO BE THE CAUSE OF THE EXCESS DISTORTION.  THIS PROVED INCORRECT AFTER UNIT # 2

FLANGE ALSO DISTORTED.  UNIT # 3 HAS NOT BEEN INSTALLED YET, BUT IS EXPECTED TO REACT

THE SAME.  MTM RECOMMENDS OPENING ALL NB FLANGE HOLES UP TO 5/8" AND RE-FACING THE

FLANGE FLAT AFTER ALL PORTS ARE WELDED IN PLACE (A MINIMUM THICKNESS WILL BE

NEEDED).

Doug McCorkle

Project Disposition:

Approvals:

___________________________________________

Procurement Technical Representative

____________________________________________

Responsible Line Manager:

____________________________________________

Project Quality Assurance: