PowerINSPECT

Changing the Excel Template

Introduction

When you launch the Excel Report from PowerINSPECT ,

you will produce an Inspection Report in Microsoft Excel.

The Inspection Report follows a template created in another Excel spreadsheet.

The Excel Template spreadsheet determines the content and the layout of the Inspection Report.

This document will show you how to make these changes to Excel Templates.

Where Files are saved

Any templates supplied with PowerINSPECT are in the same directory.

If you create any new templates, you should “Save as” in that same directory.

PowerINSPECT is normally found in C:\dcam\product

Within the PowerINSPECT folder there should be a sub-folder called “Template.”  This is where the Excel templates should be saved.

Important

If you open an Excel template file you will see a number of ‘tabs’ at the bottom of the window.  Clicking on these tabs will allow you to transfer between different pages or ‘worksheets’ within the document.

The different worksheets have been carefully designed to produce reports on all the different inspection features in PowerINSPECT.

You should make changes to only two worksheets:

The Template (shown above), and

The Header (shown below)

Making changes to an Excel Report

As described in the Introduction there are three types of information in the Excel Report:

Information which is the same every time the report is printed

This includes things like your company logos, address and contact details.

This information is often right at the top of the report and usually gives information about your company- not the contents of the report.

Information which sometimes changes for different parts or different customers

This will usually identify who the report is for, and what part it describes.

It will normally be near the top of the Inspection Report (what we would consider the ‘Header’), or at the bottom.

The layout and contents may need to change according to customer requirements, as the following examples show.

The actual contents of these sections are determined by the user in the PowerINSPECT session:

This is determined at the beginning of the inspection but can be modified later.

# Inspection Results from PowerINSPECT

The actual PowerINSPECT inspection data is the third part of the report.

I Want To Make Changes to:

## The Company Logo

This is:

“Information which is the same every time the report is printed”

There are two aspects to the company logo:

- The picture file

- The positioning in the template

## The Picture File

Go into the ‘Template’ worksheet.

Find the logo picture

When you select the logo:

- It will be surrounded with selection boxes

- A Picture toolbar will be displayed

- The “Name Box” will show “LOGO”

Changing the logo Picture

1	Delete the old logo

2	Insert a new logo with the Insert Menu

Choose the logo and insert it

3	Name the new logo “LOGO”

### Resizing the Logo

The Template has custom features to allow you to make changes like this.

A toolbar has been provided for these features.

Click on “EditZone” to resize the logo.

This brings up the “Zone Edition” box.

Click on “LOGO Position”

This will show where the logo is to be drawn.  In this case the logo would be drawn in the highlighted box, from row 6 column 2 to row 7 column 11.

This is why the Header.LogoPosition box ends in R6C2:R7C11.  It runs from row 6 column 2 to row 7 column 11.

Note that the logo will cover this entire area.  If we print this report as it is now, it will come out like this.

The logo is scaled to fit the defined area.

We need to redefine the logo area to keep the logo in proportion.  We might use row 6 column 2 to row 7 column 3 for this logo.

Click on “EditZone” again and redefine a new area.

Click “Define” and this will change the area.

A confirmation box will appear.

Click OK and the area will be changed.

You then need to click on the X in the top left hand corner of the “Zone Edition” box to remove it.

The logo will then fill this new area when you generate an Excel report.

For ease of use it is worth moving and resizing the picture to fit approximately in the printing area, by dragging and clicking.

It is not actually necessary to do this- but it makes it a lot easier to understand!

# Text boxes

The Report is produced in Microsoft Excel.

It is started either with the

(Excel Report Button

or with

(File- Generate Excel Report

An Inspection Report normally consists of:

Information which is the same every time the report is printed

Information which sometimes changes for different parts or different customers

Inspection Results from PowerINSPECT- these are different every time

This is a Template.

It is very similar to the report.

You can make changes to the Inspection Report by making changes to the Excel spreadsheet Template.

You can make new Inspection Reports by copying an Excel spreadsheet Template and making changes to the copy.

Template choice

Header information

The inspection data consists of point coordinate data and graphs.

Normally only the presentation needs to be changed.

Picture Toolbar

Logo is selected

Name Box

Name Box

Type “LOGO” in Name Box

The logo scales to fit the area defined.

This is the template.

The logo area is shown highlighted.

This is the Excel Report as printed.

The logo fits in the area.

This is the template, with the logo resized by hand.