Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

# Text boxes

- MC Fit-up Check & Surface Insulation

(	Verify MC’s of MCHP will come together (Gross Fitup)

- Pre-Measurement of MHCP Type A/B/C Coil Flanges & Interfacing Type Type A Coil Flange

(	Verify that the individual coils can be racked into proper shape.

(	Verify that metrology measurements can be accurately taken and reproduced.

- Alumina Shim Sizing & Preparation

- Define shim sizes and compress to arrive at satisfactory shim set for MCHP assembly.

- Pre-Installation Station 2 Set-up (for First Article Only)

- Tooling/fixtures setup.

- Pre-Assembly A-A  - (DELETED – ACCOMPLISHED IN STEP 2.0)

- Tooling not rigid enough - RETIRED

- Coils still to flexible - RETIRED

- Alignment not within tolerances bars- RETIRED

- Shim thiucknesses do not match inventory

- Tooling Rigidity – wedges determined to be adequate

- Coil Flexibility – physically racked (twisted) coils to re-establish coordinate system

- Alignment – iterated until met requirements

- Shims – fabricate/order new shims

Alignment not within tolerances

- Alignment not within tolerances

- Weld distortion excessive

- Rescan components & perform “best fit” of MCHP.

- Back Office assess tolerance recovery by realignment

- Investigate mitigation by trim coil design

- Alignment – iterate until meet requirements

  - Weld distortions

    - Install wing chairs to offset distortions

    - Project determine path forward if unable to meet tolerance requirements.

    - If required, coil welds can be ground out & coil separated

- A-B Coil Assembly to C Coil

- Attach A-B assembly & fixture to another 20° wedge.

- Using templates, mark nose shim & puck locations on B coil.

- Place shims (4-8) onto B coil, lower C coil into place, &  align C  coil to A-B assembly (±  0.060” X-Y /±0.002”Z).

- Measure shim puck height at a number of points around puck, raise C coil & install nose shims, lightly tack weld flex nose shims.

- Lift C & flip to ready for nose welding.

- Install remaining shims, studs, supernuts and torque to 50%.

- Adjust C coil to install nose shims and measure.

- Recheck A-B assembly alignment during these processes

- Re-measure B coil fiducials – weld Type B flex shims to plasma side, recheck fiducials. Back Office assess part for compliance.

- Once initial B welding & alignment efforts completed, Back Office assess part for compliance.

- Measure C coil fiducials – weld Type C flex shims to plasma side, recheck fiducials. Back Office assess part for compliance.

- Remove alumina shims on B coil as needed to facilitate re-mating of  C coil to A-B assembly. Re-measure alignment.

- One hole at a time, remove supernut & measure hole eccentricity. Select bushing & machine as necessary & install and re-tighten to 50% torque and recheck alignment.

- Install wing support hardware & tighten all bolts to final torque.

- Weld A/B nose region solenoid side & re-measure.

- Alignment not within tolerances

- Weld distortion excessive

- Alignment – iterate until meet requirements

  - Weld distortions

    - Internally Reinforce/Rack MC

    - Back Office determine path forward if unable to meet tolerance requirements.

Shim bags rupture when filling

- Each shim bag will be pre-qualified

- Wing chair could be installed in compression

- Determine if replacement of shim bags needed => will require taking coil all apart.

Side-A

- Inflate All Shim Bags

- Fill wing bladders & cure

- Install Trim Coils – (MOVED TO STATION 5)

- Complete Local Services  & Interface Details

- Inject sealant to fill all shim spaces to trap VV/MC insulation.

- Final Measurements & Transfer MCHP to Holding Area

- Measure all tooling balls & record/save data & run copies of installation procedures.

- Install/identify 3 primary fiducials to be used on Station 3.

- Do final measurements & record results. Measure bolt lengths on all tension fasteners & record/save results.

- Mark part, install base supports, remove from stand & measure weight of completed MCHP.  Remove to holding area.

REPEAT FOR EACH SUBSEQUENT MCHP

SideB

- A-B Modular Coil Assembly

- Rack A coil & measure fiducials.

- Using templates, mark nose shim & puck locations.

- Place shims (4-8) onto A coil, lower B coil into place, &  align B  coil to A coil (±  0.060” X-Y /±0.002”Z).

- Measure shim puck height at a number of points around puck, raise B coil & install nose shims, lightly tack weld flex nose shims.

- Lift B & flip to ready for nose welding.

- Install remaining shims, studs, supernuts and torque to 50%.

- Adjust B coil to install nose shims and measure.

- Recheck A alignment during these processes

- Re-measure A coil fiducials – weld Type A flex shims to plasma side, recheck fiducials. Back Office assess part for compliance.

- Once initial A welding & alignment efforts completed, Back Office assess part for compliance.

- Measure B coil fiducials – weld Type B flex shims to plasma side, recheck fiducials. Back Office assess part for compliance.

- Remove alumina shims on A coil as needed to facilitate re-mating of  B coil to A coil. Re-measure alignment.

- One hole at a time, remove supernut & measure hole eccentricity. Select bushing & machine as necessary & install and re-tighten to 50% torque and recheck alignment.

- Install wing support hardware & tighten all bolts to final torque.

- Weld A/B nose region solenoid side & re-measure.

NONE IDENTIFIED

Side-B

Side-A

Figure 2.  MCHP Component Winding Forms

Type-C

Type-B

Type-A