| LIFT TITLE: Lifting the Modular Coil Winding Form | Effective Date: | Date Performed: |
| --- | --- | --- |
| LIFT PROCEDURE NO.D -L-NCSX-983 AREA: NCSX Coil Manufacturing Facility | Repetitive Lift Expiration Date: | Approved: LIFT MANAGER |
| DISASSEMBLY PROCESS COMPLETED PIC: PROCEDURE PREREQUISITES COMPLETED QC: |
| M. Viola presence required: rotation DESCRIPTION: WEIGHT: 6200 Lbs. (max.) DETERMINED BY: Calculations Sketch of rigging shall include: Crane Capacity, Hook Load, All Rigging, Lift Height, Flight Plan Sketch of equipment shall include: Dimensions, Bolts Removed, Allowable Tilt |
| CRANE OPERATOR RIGGING TEAM (print) (print) APPROVED: QRS PIC LIFT ENGINEER (Rigged per sketch) (Equipment ready to lift) (Qualification/inspection complete) |

. . . PERFORM LIFT. . .  PERFORM LIFT . . . PERFORM LIFT . . .

Equipment is secure and rigging may be removed: PIC: Date Performed:

LIFT DATA SHEET AND ALL DATA TO BE RETURNED TO PPPL OPERATIONS CENTER.

# Text boxes

(2) Chain-falls
( 2-ton capacity each

1

1) Lift Coil

2) Extend chain-fall (1) to upend coil until slack and disconnect

3) Adjust chain-fall (2) to lift coil

4) Reconnect chain-fall (1) on opposite side bottom. Adjust choke as needed.

5) Extend chain-fall (2) and or retract chain-fall (1) to level coil.

(4) slings various lengths vertical capacity ( 5,300 lbs. each [Green]

2

(8) Lift nut or Lift fixture plates, 
5/8” or ¾” swivel hoist ring, 
6 ½ ton shackle 
(as needed)

Connect slings to plate or nut on bottom of flange or chokes, if  necessary.

Coil No.

_____________

(3) sling ~8’ choke capacity ( 8,500 lbs. each [tan]

1 ¼” shackle

Point chokes opposite of direction of rotation.

Alternatively, If necessary, offset single top sling to one side opposite where lift nut may be used.  Use third chain fall connected to lift nut to control balance of coil.