| LIFT TITLE: Lifting the Completed Modular Coil | Effective Date: | Date Performed: |
| --- | --- | --- |
| LIFT PROCEDURE NO.D -L-NCSX-983 AREA: NCSX Manufacturing Facility | Repetitive Lift Expiration Date: | Approved: LIFT MANAGER |
| DISASSEMBLY PROCESS COMPLETED PIC: PROCEDURE PREREQUISITES COMPLETED QC: |
| DESCRIPTION: WEIGHT: 7000 Lbs. (max.) DETERMINED BY: Calculations Sketch of rigging shall include: Crane Capacity, Hook Load, All Rigging, Lift Height, Flight Plan Sketch of equipment shall include: Dimensions, Bolts Removed, Allowable Tilt |
| CRANE OPERATOR RIGGING TEAM (print) (print) APPROVED: QRS PIC LIFT ENGINEER (Rigged per sketch) (Equipment ready to lift) (Qualification/inspection complete) |

. . . PERFORM LIFT. . .  PERFORM LIFT . . . PERFORM LIFT . . .

Equipment is secure and rigging may be removed: PIC: Date Performed:

LIFT DATA SHEET AND ALL DATA TO BE RETURNED TO PPPL OPERATIONS CENTER.

# Text boxes

(3) Chain-hoists 
( 3-ton capacity each

1

1) Lift Coil

2) Extend motorized chain-fall or lower manual chain. to lower coil until slack and disconnect

3) Reconnect on opposite side and retract motorized chain-fall. May need to lower manual chain hoists to level coil.

(3) slings capacity (5300 each [green]

Motorized 2’ longer to allow for drawing the sling through the other chain hoists

(1) Lift nut and (2) 1” swivel hoist rings, to center of leg bottoms,

6 ½ ton shackles 
(as needed)

Coil No.

___________

(3) slings capacity (8400 each [yellow]