# Week of 11/13/06

PPPL MCWF Quality Notes

Tuesday Teleconference 11/14 9 AM EST (877) 952-1506, Passcode: 833648

- Closed Items:

  - NC 20676, for discrepant radii at base of the “T” on B-2 (step 130), is Closed.

  - PPPL sent approval of the B1 documentation package on 11/10/06.

- Pending from EIO:

  - (EIO, MTM) Provide documentation of completion of corrective action for EIO CA 090606(NCR) for B-3 & B-6 Vacuum Vessel support pads deviations.  
Status: (Open) MTM confirms that the center hole position is fixed but the tapped hole pattern is being shifted as needed (applies to all Type B castings). EIO/MTM will provide proposed shifted locations prior to drilling.  On B3 & B6 it’s likely that one hole cannot be drilled (corner missing).  The CA will remain open until after B6 is completed.

  - (EIO, MTM) MTM will send IDC’s with Tee radius check added. 
Status: (Open).   NCR was also received;  Will be reviewed and dispositioned today.

- Pending from PPPL

  - Issue ECN for the elimination of Thred Gard use on Drawings SE141-101, 102, 103.
Status: (Open) ECN 5197 was generated and is in the processing cycle.  A copy of it will be sent to EIO later this week.

  - PPPL to process EIO RFD for Type B Thin Wall conditions.
Status: (New) EIO RFD 110806 was regenerated as NCSX RFD-14-026 and is in the approval cycle. Note that EIO is holding final submission of B-2 data package until RFD is approved since this RFD will be placed in Doc packages B-2 thru B-6.  ECN 5185 covers the required drawing note changes. RFD will be sent today.

  - PPPL issued ECN 5185 which addresses clearance for counter-bored flange holes & clearance/notching for support post/G11 lead block plate interference.  
Status: (Closed) A copy was transmitted to EIO on 11/13.

  - Disposition NC 20471 for RT indications at Holes 26-30 and Holes 41-45. 
Status: (Open) Discuss at Tuesday Teleconference.

- Discussion Topics For Next Telecon -

  - Results of A-4 Inspection results (including 3.4, above)