# Week of 11/20/06

PPPL MCWF Quality Notes

Tuesday Teleconference 11/21 9 AM EST (877) 952-1506, Passcode: 833648

- Closed Items:

  - PPPL provided EIO with ECN 5185 which addresses clearance for counter-bored flange holes & clearance/notching for support post/G11 lead block plate interference.

- Pending from EIO:

  - (EIO, MTM) Provide documentation of completion of corrective action for EIO CA 090606(NCR) for B-3 & B-6 Vacuum Vessel support pads deviations.  
Status: (Open) MTM confirms that the center hole position is fixed but the tapped hole pattern is being shifted as needed (applies to all Type B castings). EIO/MTM will provide proposed shifted locations prior to drilling.  On B3 & B6 it’s likely that one hole cannot be drilled (corner missing).  The CA will remain open until after B6 is completed.

  - (EIO, MTM) MTM to provide completed IDC with Tee radius check with the A-4 documentation package. 
Status: (Open).

- Pending from PPPL

  - Issue ECN for the elimination of Thred Gard use on Drawings SE141-101, 102, 103.
Status: (No Change) ECN 5197 was generated and is in the processing cycle.

  - PPPL to process EIO RFD for Type B Thin Wall conditions.
Status: (No Change) EIO RFD 110806 was regenerated as NCSX RFD-14-026 and is in the approval cycle. Note that EIO is holding final submission of B-2 data package until RFD is approved since this RFD will be placed in Doc packages B-2 thru B-6.

  - Provide signed copies of A-4 NCR’s which were all dispositioned during QA meetings on 11/14.
3.4.1 NC 20733 for penetrant inspection failures
3.4.2 NC 20741 for RT failures
3.4.3 NC 20759 for dimensional OT
3.4.4 NC 20761 for visual inspection
Status: (Open)

- Discussion Topics For Next Telecon -