PPPL MCWF Quality Notes Update 9/21/06

No Tuesday Teleconference on 9/26/06

1        Closed Items:

1.1      MTM NC20338 corrective action (B-2 lead pad deviation) closed – replaced by NC 20475.

.2        Pending from EIO:

2.1       (EIO) Address NC discrepancies in A-1 Documentation Package.
Status: (Open)  Will be addressed on Roy’s return.

2.2      (EIO, MTM) Provide documentation of completion of corrective action for NC20449 (mis-drilled holes on B-2).
Status: (New)

2.3      (EIO, MTM) Provide documentation of completion of corrective action for NCR NC 20475 for Lead Block Deviations on B-1 & B-2.
Status: (New)

2.4      (EIO, MTM) Share results of investigation and corrective actions taken regarding recent errors. 
  Gear damage

Mis-drilled holes

Set-up instruction misinterpretation in Lead areas

Shearing of Head bolts?

3        Pending from PPPL

3.1     Review Final Documentation Packages

3.1.1    A-1
Status: (Open) – NC comments sent to EIO.

3.1.2    A-2
Status: (No Change) –

3.1.3    A-3
Status: (No Change) –

3.1.4    B-1 (posted 9/1)
Status: (No Change) –

3.2      Disposition EIO CA 090606(NCR) for B-3 & B-6 Vacuum Vessel support pads deviations.
Status: (No Change)  In process –RFD initiated

3.3      Issue, and provide copy to EIO, Request For Deviation (RFD) for change to mounting holes on VV pads on B-Type castings.
Status: (New)

3.4      Disposition NCR NC 20483 for rejectable B-1 PT indications.
Status: (New)

3.5      Disposition NCR NC 20487 for B-1 Poloidal Break Gap requirements exceeded.
Status: (New)

Thanks,

Frank

Frank Malinowski - MS01

The DOE Princeton Plasma Physics Lab

PO Box 451

Princeton, NJ 08543-0451

==============================================================

PH (609) 243-2203 FAX (609) 243-3366 http://www.pppl.gov/

==============================================================