The hole pattern on the pad between the lead block slots is not centered on the cast pad.  In order to center the pattern on the pad it would need to be shifted approximately .350” as shown in the picture below.

I am proposing the following options:

- Shift the hole pattern .350” in order to center the pattern on the block

or

- Shift the hole pattern and the lead block slots .350”.  (This would shift the location of the lead block openings relative to the finished T) – See figure 1.

or

- Weld build up the edge of the block to accommodate the three tapped holes that are currently shown off the edge.

Wide View of Current Part Orientation

EIO Addendum - View of the Model from Inside

Figure 1 – Lead bock slot view from inside