Type B1 and B2 Connection Block Repair

B1:

- Machine the slots to include the correct boundaries.

- Machine the pad base to the correct height.

- Fill in whatever remains of the holes with weld.

- Face off the pad.

B2:

- Pad will be per the print.  Holes were not drilled, so they will be located per the print.

- Machine the slots to include the correct boundaries