| NCSX RFD Part I | Number: | RFD Description: A1 Counterbore Clearance |
| --- | --- | --- |
| Initiator: Mike Griffith | Organization: Major Tool and Machine |
| List of Impacted Documents: (Specification, MIT/QA Plan, SOW, drawing, etc.) |
| Cost Impact: (If none, so state) |
| Schedule Impact: (If none, so state: |
| Quality Impact: (If none, so state): |
| State Requirement Deviation is Requested For: (Specification, MIT/QA Plan, SOW, drawing, etc.) |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate to support deviation request.) Request deviation from requirement to grind a 3”diameter area 2” above the counterbore surface for the 1.885” thru holes in both the E and D flanges. There is 1 hole in the D flange and 6 holes in the E flange that will require excessive grinding to provide clearance for the 3” diameter gage. Major Tool proposes that these 6 holes remain as machined and PPPL fabricate threaded plugs to be welded into the counterbores. |
| Attachments: Counterbore clearance map. |
| Initiator Signature: Date: |