| NCSX RFD | Number: NCSX-RFD-12-010 | RFD Description: NCSX NB Seal / Cover Plate Assembly |
| --- | --- | --- |
| Initiator: Doug McCorkle | Organization: Major Tool and Machine |
| List of Impacted Documents: SE122-173 |
| Cost Impact: (If none, so state) NONE |
| Schedule Impact: (If none, so state) NONE |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state) None |
| Full Description of the Deviation Requested: (Use continuation pages, e-mails, letter, sketches, etc. as needed and include amplifying information as appropriate) DEVIATION REQUESTED: Modification required to existing Seal Retainer SE122-173 to alleviate interference with undersize metal seal. Request authorization to grind the outside profile (maintaining the angle and surface finish) inward to reduce interference created by undersized metal o-ring. JUSTIFICATON FOR DEVIATION REQUEST: Part cannot be assembled under current condition. |
| Attachments: See attached photographs showing interference. |
| Initiator Signature: Doug McCorkle Date: 20Jan2006 |

NB Seal/Cover Plate Assembly

NB Seal/Cover Plate Assembly Detail of Interference Area

Circled Area Shows Specific Interference Area

| NCSX RFD Part II | Number: 12-010 | RFD Description: NCSX NB Seal / Cover Plate Assembly |
| --- | --- | --- |
| RLM: Brad Nelson | Organization: ORNL |
| Impact on Interfaces with Other WBS Elements/Items: (If none, so state): NONE |
| RLM Recommendation: Approve Do Not Approve Additional remarks: Art Brooks: N/A Paul Goranson: Radii may be completely cut off if needed. Bevel may be ground as needed. Retainers are only to assist in assembly. Tongue depressors may even be used to temporarily hold seals in place in lieu of retainer until flange cover is installed and compresses seal enough to hold in place. Does this Change Impact Material Already Procured or Parts/Assemblies Already Assembled/Manufactured using this Material: Yes No If “Yes”, what is the recommended disposition of this material/part/assembly? Modify as above per Paul Goranson |
| RLM Signature: |
| Project Disposition: Approved. No ECP required. However, an ECN will be processed by January 31st to reflect this change. Approved. ECP -044 assigned. ECN will need to be issued and then CSPEC revised to pick up the revised drawing rev. NCSX Systems Engineering Support Manager Not Approved. Reason(s) for disapproval: |