NCSX Fault Analysis Model

Descriptions of EM Analysis Model

- Model includes modular coils, TF coils, PF1 to PF6 coils and plasma current in one field period.

- Any one PF coil and/or one TF coil may be selected to have zero currents

- For PF fault analysis, it represents a real case

- For TF fault analysis , it represents three cyclically symmetric TF coils have zero currents, one in each field period..

To Make An Fault Analysis for A Current Scenario

Step 1: In the input file, entering the turn currents of all conductor currents

Step 2: Select the particular coil that has no current

- For TF coil, input tff = n1, where n1 = 1,2,3,4,5,or 6

- For PF coil, input pff = n2, where n2 = 79,80,81,5,3,1 for upper PF1 to PF6, respectively and n2 = 82,83,84,6,4,2 for lower PF1 to PF6 respectively.

An example of the input file is shown in the file “itg_model_fault-em.txt”.  This has the current scenario for 2T High Beta scenario at 0.197 second.  The selections of tff = 2 and pff=3 mean that the second TF coil and the upper PF5 both have zero currents.

The required command and database files needed in the analysis are (see Folder “Files_for_Running_Fault_Analysis):

- itg_model_fault-em.txt:  A fault analysis for 2T high beta current scenario at 0.197 second

- tf_pf_wg_mc.db:	EM analysis model

Notes:

The above files may also be found in the following folder on HM Fan’s Computer::

C:\Documents and Settings\hmfan\My Documents\ansys7.1_files\mc-shell_FDR\shell0408/new-tf_pf_mcwf

The output file “file.db” is the results of fault analysis

Notes:

- The user who will make a new run should set up an ANSYS working directory

- The sub-working directory is new-tf_pf_mcwf

- The version of ANSYS is v11