NCSX

Design Basis Analysis

DRAFT-B

Base Support Structure Analysis

NCSX-CALC-17-001-00

27 May 2008

Prepared by:

_______________________________________

F. Dahlgren, PPPL

I have reviewed this calculation and, to my professional satisfaction, it is properly performed and correct.  I concur with analysis methodology and inputs and with the reasonableness of the results and their interpretation.

Reviewed by:

_______________________________________

H.M. Fan, PPPL, Engineer

Introduction

The Base Support Structure is connected to the Coil Support Structure (WBS 15) at six locations, and provides the load path for the dead weight of the entire NCSX core, which includes the MCWF shell and modular coils as well as the conventional PF, TF, and Trim coils. In addition, it must also support the weight of the cryostat and many of the coil services, which include the cryogen feeder lines and coil bus work.  The outboard support columns are located 120 degrees apart at the C-C MCWF joints and at an elevation of 94” and at a nominal radius of 79.5”. The inner support columns are located at 120 degree intervals at the A-A MCWF joints at an elevation of 90” and a nominal radius of 29.5”. These interfaces must provide structural continuity between the floor, base structure, and coil structure for gravity and seismic loading. All EM loads will be reacted within the MC structure and TF-PF interconnections. The six interfaces at the base/coil support structure will be bolted with G11 insulating plates, washers, and bushings, to provide both electrical isolation for ground loops, and thermal insulation to minimize heat transfer from the warmer base structure to the cold coil support structure. Spherical bearings will be used to allow for any angular misalignments between the MCWF/core structure and base supports and will also supress moment constraints being transmitted to the MCWF due to rotational flexing of the modular coil structural shell. To provide radial compliance between the core and supporting structure, a low friction PTFE surface will be used between the column pedestal and spherical bearing lower clevis base plate. Z-shaped channels bolted to the base support pedestals will capture the sliding lower clevises to restrict lateral (circumferential) sliding and any vertical lifting of the core (resulting from seismic over-turning motions). All gravity loads and loads from any seismic events are reacted through these interfaces, through the base support columns and base frames to the test cell floor, and ultimately, to the C-Site basement floor.

The current analysis evaluates the adequacy of the base support frames, anchors, and columns when subjected to normal gravity and seismic loading. The analysis of the MCWF/core-base structure interface assembly (including the spherical bearing housing) is covered in the Coil Support Structure Design Basis Analysis (NCSX-CALC-15-001-00).

Base Support Structure For NCSX                                  MCWF/core-Base Structure Interface

Methodology

The analysis of the base support structure was accomplished using the ANSYS Finite Element Analysis program version 11.1. The FEA model of the base supports applies loads from gravity,  and a static seismic loading based on the NCSX Seismic Design Criteria Document  (NCSX-CRIT-SEIS-00).

Assumptions

The full weight of the stellarator core is assumed to be 300 kips (loads have been calculated from CAD models of various components and estimated for some components which are not yet finalized with a 5% additional factor added – see Appendix II).

The boundary conditions at the bottom of the building columns supporting the test cell floor are assumed to be fixed in all 6 degrees of freedom implying an infinitely stiff basement floor. Symmetry boundary conditions are applied around the perimeter of the test cell floor to account for the remaining floor and building structure. The gravity loading is assumed to be uniformly applied at the top of the column pedestals for the outer columns. The offset from the centroid of the support columns at the inner A-A supports result in a additional radial load necessary to react the moment arising from the minor eccentric loading there. Rigid beams attached to a concentrated mass, representing the full mass located at the C.G. of the stellarator core, apply the horizontal seismic accelerations and moments to the tops of the column pedestals. These beams are attached to the column pedestals via coupled nodes with only three translational DOFs which assumes that the spherical bearings can only transmit translational forces and no moments.  Room temperature (295 K) isotropic material properties are assumed for all components.

Estainless = 29 e 6  psi (200GPa) (all base support structural components)

Econcrete =  3.8 e 6 psi (26.2GPa)

EA36-stl  = 30 e 6 psi (207 GPa)

µ= 0.2 friction coefficient floor to base

Description

A finite element model of the NCSX base support structure including a portion of the test cell floor and basement structure is shown in Figure 1 below. The model uses 20-node hexahedral solid (brick) elements for the column and beam webs, flanges, gussets, and end plates. The test cell floor, which is 12 inch thick 3,000 lb reinforced concrete, also is modeled using 20-node brick elements (yellow elements in Fig.1), and the appropriate elastic modulus. The floor girders, stringers, and columns supporting the floor (light blue, purple, and red lines in Fig. 1) are modeled as beams with the appropriate section modulus and properties.

Building Steel is modeled with beam188 beam elements - Sections:

P3-columns 14WF-127

G1-girders   27WF-124

S1-stringers 12WF-106

The outer machine column lateral bracing (light blue diagonals in Fig.1), use angle beam elements with the appropriate section properties. The base to  floor interface surfaces are attached with standard contact elements which allow for sliding and separation in the non-linear solution. A conservative value of 0.2 was chosen for the coefficient of friction between the concrete floor and the bottom flange of the  base support beams. Coincident nodes at the anchor bolt locations are coupled together to simulate the bolted connections to the anchors, which will be embedded in the concrete floor. Semi-rigid beams connect the top column plates to the stellarator core  c.g., which is used to apply the static horizontal loads for the seismic runs.

Figure 1.  ANSYS FEA Model of the Base Supports & Test Cell Floor (full-base-suppt-model-F4h)

Based on CAD and ANSYS models, the dead load of the entire Stellarator core was initially determined to be approximately 240 kips without the vessel liner, trim coils, coil services, neutral beam duct, and diagnostics. The dead load distribution between the outer and inner supports was determined from results of  the integrated global model of the Stellarator core which is shown in tabular form in Appendix I with a factor of 1.25 to account for the items mentioned above which are not yet designed. Appendix II is a summary of all dead loads in the machine core including estimate of the TBD components. To be conservative a factor of 5% over these estimates was used for this analysis. The complete (estimated dead load, including the 5%, is 300 kips). In general, based on Appendix I results, the load will shift about 3.2 kips to the outboard supports due to EM loading and cool-down, producing a 53.2-46.8 kip load split outboard to inboard during machine operations and about 51.6-48.4 kip split when sitting cold w/o EM loads applied.

Results

Load Case 1: 50 kip Inboard & Outboard Support Loading

Figure 2 below is a contour plot of the SRSS displacements due to the room temperature gravity loading condition. The load distribution is essentially uniform at 50kips per support.

Figure 2. SRSS Displacements due to gravity loading –Stellarator core at room temperature

Figure 3 is a contour plot of the vertical (dz) displacements due to room temperature gravity loading. The maximum vertical displacement is -0.083” occurring at the top pedestals of the west inner support columns. The one est column deflects about 0.010” less. The test cell floor peak vertical displacement  is 0.042” and occurs at the edges of the middle floor cutout as shown by the darker blue contour in figure 4.

Figure 3 Vertical (dz) displacement contours -stellarator core at room temperature

Figure 4. Test Cell Floor Vertical (dz) displacement contours -stellarator core at room temperature

The Tresca stress contours are plotted for the room temperature gravity loading in Figure 5 and indicate a peak stress of  12.4 ksi at the anchor points of the inner base beam. The stresses in the columns are seen to be in the range of 2 to 4 ksi. The maximum stress intensity of 9 ksi in the column support assemblies is at the center of the inner support top plates.

Figure 5. Tresca stress contours -stellarator core at room temperature -peak stress is 12.4 ksi

When the stellarator core is cooled down to 77 K there is a redistribution of loads which increases the gravity loading on the outboard column supports by about 3 kips and reduces the inboard column load by the same amount. When the core is cold the outboard supports now have a total loading of 53 kip per support and the inboard columns have a 47 kip load.

Load Case 2: 46.87 kip Inboard, &  53.13 kip Outboard Support Loading

For load case 2 there was a minor model change, re-locating the girder,  stringer, and top column nodes to be co-planar with the bottom nodes of the test cell floor slabs, and off-setting the beam origins to their proper heights. The model, shown in figure 6 below, should more accurately represent the composite floor-beam stiffness.

The vertical displacement contours of the floor for load case 2 are shown in figure 7. The maximum displacement of the floor, shown as the darker blue contour, is 0.025”.

Figure 6. Re-modeled floor girders & stringers (full-base-suppt-model-F4j)

Figure 7. Vertical displacements of the test cell floor – Load Case 2

The vertical displacement contours of the full model load case 2 are shown in figure 8. The peak displacement is 0.066” and occurs at the top of the two inner columns located over one of the central floor openings and is represented by the dark blue contours.

Figure 8. Vertical displacements of the base support structure – Load Case 2

The SRSS (vector sum) displacement contours for load case 2 are shown in figure 9. The maximum displacement of ~0.08” is at the top of the two inboard support pedestals over the floor cutout shown in red.

Figure 9. SRSS Displacement contours of base supports – Load Case 2

The Tresca stress contours for the floor and base supports for load case 2 are shown in figure 10 below. The peak stress is about 16 ksi (110MPa) and occurs at the upper inboard column pedestal at the corner intersection of the web, flange, and top pedestal. This single point peak coincides with the vertex of a pentahedral transition element, which tends to be overly stiff thereby over estimating the stress at this point. In general the stresses in the base supports are in the range of 3ksi to 12ksi (21 to 83 MPa), with the major portion of the columns less than 7 ksi (<50 MPa).

Figure 10. Tresca Stress contours for Load Case 2

Load Case 3: Seismic Loading with 46.87 kip Inboard, &  53.13 kip Outboard Support:

The seismic loading considered is based on the NCSX Seismic Design Criteria (NCSX-CRIT-SEIS-00), which requires a .171 g static load applied at the machine core c.g. per Table I. A modal analysis predicts the primary flexible mode will be @ 1.7 Hz as a lateral flex at 30 degrees off the X-axis.

TABLE I  (REF. NCSX-CRIT-SEIS-00)

This translates into a static horizontal load of 51,300 lbs applied at a height of 15.2 feet above the test cell floor. To model the machine core, six semi-rigid beams were added to the base support structure model to represent the approximate stiffness of the core. The beam elements extend from 4” above the support column pedestals to the machine c.g. located 15.2 feet above the floor at the machine center. The revised seismic model is shown below in figure 11. To represent the radially oriented sliding base of the machine supports the lower nodes of the six beams are coupled vertically and circumferentially to nodes on the pedestals which represent the radial guides which physically capture the sliding bases (these guides permit radial motion while restraining circumferential and vertical motion). The static horizontal load is applied in the North-South and East-West directions as two separate loading conditions. A vertical load of 1.1g is also applied at machine c.g.

Figure 11. Seismic model of NCSX machine base supports

Displacement results of the east-west acceleration loading (X-dir.) are shown in figure 12. The SRSS (vector sum) displacement at the c.g. is 0.11”, primarily, as you would expect, in the x direction. The Tresca stress contours for this loading are shown in figure 13 and indicate a peak stress of 17.2 ksi (118.6 Mpa). As can be seen in the insert, the location is at the corner/edge interface of  one of the lateral brace brackets and is largely the result of local modeling issue (due to how the nodal points of these brackets are coupled to the top of the base support beam flange). Figure 14 shows the SRSS displacements for a north-south static seismic loading and indicates the peak displacement of the c.g. is, again as expected, 0.11” primarily in the north-south direction. The Tresca stress contours, plotted in figure 15, indicate a peak stress of 18.4 ksi (126 MPa) at the inboard base beam/floor interface just below the reinforcing rib (see the enlarged insert in figure 15). This peak is highly localized with the remaining structure stresses falling in the range of  8 to 12 ksi (55 to 83 MPa).

Figure 12. SRSS Displacements due to an east-west static seismic loading condition

Figure 13. Tresca Stress contours due to east-west seismic loading condition

Figure 15. Below is contour plot of the vector sum displacements resulting from an applied static seismic loading in the north-south direction. The peak displacement, at the machine c.g., is again 0.11” in the north south direction.

Figure 14. SRSS Displacements for north-south seismic loading condition

Figure 15. Tresca Stress contours for north-south seismic loading condition

Anchoring:

Buckling:

Fatigue:

Conclusions:

The base support structure meets the design allowables (Sm) for the NCSX project which for primary stresses is 2/3rd the minimum yield stress of the materials at temperature. For the 304L and 316L structurals this Sm is 16.6 ksi (110 MPa). Under seismic loading conditions the peak stress intensity is 18.4 ksi (126.9 MPa) occurring at a bracket-base beam flange interface. The stress in this area is artificially higher due to constraints imposed by coupling the bracket end nodes to nodes on the top flange surface. In general the stress due to seismic loading is well below the design allowable (1.5 Sm = 25 ksi, for bending). Buckling margins for columns exceed the project requirements (> 5). The room temperature lower sigma fatigue curve indicates we have substantial margin on the 2xS @130,000 cycles and  20x life requirements.

Appendix I

| New model - Hexahedral-shaped TF bracket, higher weight and reviced Ex and Alpx |
| --- |
| Loads | Items | Unit | Model 1R | Remarks | Comments |
| Dead load | D max | mm | 3.02E-01 | w/o support block | Dmax at PF6 |
| ● w/o Wt. increase | DZ | mm | (-0.292 to 0.0314) | w/o support block |  |
| ● stellalloy E=199GPa | Seqv | Pa | 1.10E+08 | PowerGraphics OFF | Max.Seqv at sup. Block |
|  | Seqv | ksi | 1.60E+01 | PowerGraphics OFF | Max.Seqv at sup. Block |
|  | OB reaction | N | 1.53E+05 |  |  |
|  | OB reaction | kip | 3.43E+01 | Total weight |  |
|  | IB reaction | N | 1.60E+05 | 3.122E+05 | G10 shim on PF6 sup. |
|  | IB reaction | kip | 3.59E+01 | 7.018E+01 | Calculated weight |
| Dead load | D max | mm | 3.34E-01 | w/o support block | Dmax at PF6 |
| ● DL Factor = 1.14 | DZ | mm | (-0.324 - 0.0310) | w/o support block |  |
| ● stellalloy E=199GPa | Seqv | Pa | 9.68E+07 | PowerGraphics OFF | Max.Seqv at sup. Block |
|  | Seqv | ksi | 1.40E+01 | PowerGraphics OFF | Max.Seqv at sup. Block |
|  | OB reaction | N | 1.82E+05 |  |  |
|  | OB reaction | kip | 4.09E+01 | Total weight |  |
|  | IB reaction | N | 1.74E+05 | 3.559E+05 | G10 shim on PF6 sup. |
|  | IB reaction | kip | 3.91E+01 | 8.001E+01 |  |
| Dead load | D max | mm | 3.33E-01 | w/o support block | Dmax at PF6 |
| ● DL Factor = 1.14 | DZ | mm | (-0.323 to 0.0314) | w/o support block |  |
| ● stellalloy E=145GPa | Seqv | Pa | 9.68E+07 | PowerGraphics OFF | Max.Seqv at sup. Block |
| ● Regular PF shim | Seqv | ksi | 1.40E+01 | PowerGraphics OFF | Max.Seqv at sup. Block |
|  | OB reaction | N | 1.74E+05 |  |  |
|  | OB reaction | kip | 3.92E+01 | Total weight |  |
|  | IB reaction | N | 1.82E+05 | 3.561E+05 | SS shim on PF6 sup. |
|  | IB reaction | kip | 4.09E+01 | 8.005E+01 |  |
| EM load | D max | mm | 2.793 | w/o support block | Type C modular coil |
| ● stellalloy E=145GPa | DZ | mm | (-0.993 - 1.359) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 4.05E+08 | PowerGraphics OFF | MCWF flange shim |
|  | Seqv | ksi | 5.87E+01 | PowerGraphics OFF |  |
|  | OB reaction | N | 6.61E+04 |  |  |
|  | OB reaction | kip | 1.49E+01 | Total weight |  |
|  | IB reaction | N | -6.62E+04 | -9.900E+01 | SS shim on PF6 sup. |
|  | IB reaction | kip | -1.49E+01 | -2.226E-02 |  |
| DL & EM | D max | mm | 2.766 | w/o support block | Dmax at MC type C |
| ● DL Factor = 1.14 | DZ | mm | (-1.152 - 1.199) | w/o support block |  |
| ● stellalloy E=145GPa | Seqv | Pa | 4.05E+08 | PowerGraphics OFF | at TF shim?, others 2.51E8 |
|  | Seqv | ksi | 5.87E+01 | PowerGraphics OFF |  |
|  | OB reaction | N | 2.40E+05 |  |  |
|  | OB reaction | kip | 5.40E+01 | Total weight |  |
|  | IB reaction | N | 1.16E+05 | 3.558E+05 | SS shim on PF6 sup. |
|  | IB reaction | kip | 2.60E+01 | 7.999E+01 |  |
| DL & Cooldown | D max | mm | 4.51 | w/o support block | Dmax at TF coil mid-plane |
| ● DL Factor = 1.14 | DZ | mm | (-1.019 - 1.144) | w/o support block |  |
| ● stellalloy E=145GPa | Seqv | Pa | 4.75E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim Gxy/50 | Seqv | ksi | 6.89E+01 | PowerGraphics OFF |  |
|  | OB reaction | N | 2.46E+05 |  |  |
|  | OB reaction | kip | 5.52E+01 | Total weight |  |
|  | IB reaction | N | 1.10E+05 | 3.559E+05 | G10 shim on PF6 sup. |
|  | IB reaction | kip | 2.48E+01 | 8.001E+01 |  |
| DL & Cooldown | D max | mm | 4.509 | w/o support block | Dmax at TF coil mid-plane |
| ● DL Factor = 1.14 | DZ | mm | (-0.990 - 1.112) | w/o support block |  |
| ● stellalloy E=145GPa | Seqv | Pa | 4.78E+08 | PowerGraphics OFF | TF bracket |
| ● Regular PF shim | Seqv | ksi | 6.93E+01 | PowerGraphics OFF |  |
|  | OB reaction | N | 2.46E+05 |  |  |
|  | OB reaction | kip | 5.52E+01 | Total weight |  |
|  | IB reaction | N | 1.10E+05 | 3.559E+05 | G10 shim on PF6 sup. |
|  | IB reaction | kip | 2.48E+01 | 8.001E+01 |  |
| DL & Cooldown | D max | mm | 4.505 | w/o support block | Dmax at TF coil mid-plane |
| ● DL Factor = 1.14 | DZ | mm | (-1.253 - 1.389) | w/o support block |  |
| ● stellalloy E=145GPa | Seqv | Pa | 6.00E+08 | PowerGraphics OFF | TF bracket |
| ● Regular PF shim | Seqv | ksi | 8.70E+01 | PowerGraphics OFF |  |
| ● PF shim COF effect | OB reaction | N | 2.46E+05 |  |  |
|  | OB reaction | kip | 5.53E+01 | Total weight |  |
|  | IB reaction | N | 1.10E+05 | 3.561E+05 | SS shim on PF6 sup. |
|  | IB reaction | kip | 2.48E+01 | 8.005E+01 |  |
| DL & Cooldown | D max | mm | 4.026 | w/o support block | Dmax at TF coil mid-plane |
| ● DL Factor = 1.14 | DZ | mm | (-1.321 - 1.465) | w/o support block |  |
| ● stellalloy E=145GPa | Seqv | Pa | 8.32E+08 | PowerGraphics OFF | TF bracket |
| ● Regular PF shim | Seqv | ksi | 1.21E+02 | PowerGraphics OFF |  |
| ● PF shim COF effect | OB reaction | N | 3.26E+05 |  |  |
| ● TF shim COF effect | OB reaction | kip | 7.32E+01 | Total weight |  |
|  | IB reaction | N | 3.04E+04 | 3.561E+05 | SS shim on PF6 sup. |
|  | IB reaction | kip | 6.83E+00 | 8.005E+01 |  |
| Cooldown | D max | mm | 4.074 | w/o support block | Dmax at TF coil mid-plane |
| ● stellalloy E=145GPa | DZ | mm | (-1.314 - 1.643) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 8.31E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 1.21E+02 | PowerGraphics OFF |  |
| ● TF shim COF effect | OB reaction | N | 1.52E+05 |  |  |
| Run: co-h2 | OB reaction | kip | 3.42E+01 | Total weight |  |
|  | IB reaction | N | -1.52E+05 | 0.000E+00 | SS shim on PF6 sup. |
|  | IB reaction | kip | -3.42E+01 | 0.000E+00 |  |
| Cooldown | D max | mm | 4.078 | w/o support block | Dmax at TF coil mid-plane |
| ● stellalloy E=145GPa | DZ | mm | (-1.445 - 1.615) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 8.31E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 1.21E+02 | PowerGraphics OFF | ALPX=2.90E-5 |
| ● TF shim COF effect | OB reaction | N | 6.91E+04 |  | ALPX=2.90E-5 |
| Vertical spring support | OB reaction | kip | 1.55E+01 | Total weight |  |
| Run: co-h3 | IB reaction | N | -6.91E+04 | 0.000E+00 | SS shim on PF6 sup. |
|  | IB reaction | kip | -1.55E+01 | 0.000E+00 |  |
| Change alpx for shim |  |  |  |  |  |
| Cooldown | D max | mm | 4.692 | w/o support block | Dmax at TF coil mid-plane |
| ● stellalloy E=145GPa | DZ | mm | (-0.932 - 1.180) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 4.71E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 6.83E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 2.08E+04 |  | ALPX=9.829E-6 |
| Vertical spring support | OB reaction | kip | 4.67E+00 | Total weight |  |
| Run: co-h3a | IB reaction | N | -2.08E+04 | 0.000E+00 | SS shim on PF6 sup. |
|  | IB reaction | kip | -4.67E+00 | 0.000E+00 |  |
| Cooldown | D max | mm | 4.667 | w/o support block | Dmax at TF coil mid-plane |
| ● stellalloy E=145GPa | DZ | mm | (-0.823 - 0.877) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 4.69E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 6.80E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 8.29E+03 |  | ALPX=9.829E-6 |
| Vertical spring support | OB reaction | kip | 1.86E+00 | Total weight |  |
| Run: co-h4 | IB reaction | N | -8.29E+03 | 0.000E+00 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | -1.86E+00 | 0.000E+00 |  |
| Dead load | D max | mm | 5.39 | w/o support block | Dmax at PF6 |
| ● stellalloy E=145GPa | DZ | mm | (-5.37 - 0) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 9.51E+07 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 1.38E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.79E+05 |  | ALPX=9.829E-6 |
| Vertical spring support | OB reaction | kip | 4.02E+01 | Total weight |  |
| Run: dl-h4 | IB reaction | N | 1.78E+05 | 3.571E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 4.01E+01 | 8.028E+01 | add wt. from PF6 links |
| EM load | D max | mm | 2.794 | w/o support block | Type C modular coil |
| ● stellalloy E=145GPa | DZ | mm | (-0.998 - 1.323) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 4.05E+08 | PowerGraphics OFF | MCWF flange shim |
| ● PF shim COF effect | Seqv | ksi | 5.87E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 2.36E+04 |  | ALPX=9.829E-6 |
| Vertical spring support | OB reaction | kip | 5.30E+00 | Total weight |  |
| Run: em-h4 | IB reaction | N | -2.37E+04 | -9.900E+01 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | -5.32E+00 | -2.226E-02 |  |
| Cooldown | D max | mm | 4.062 | w/o support block | Dmax at TF coil mid-plane |
| ● stellalloy E=145GPa | DZ | mm | (-0.942 - 0.896) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 4.64E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 6.73E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 4.42E+04 |  | ALPX=9.829E-6 |
| Vertical spring support | OB reaction | kip | 9.93E+00 | Total weight |  |
| Run: co-h4a | IB reaction | N | -4.42E+04 | 0.000E+00 | SS shim on PF6 sup. |
| w/PF6 link & bonded TF shim | IB reaction | kip | -9.93E+00 | 0.000E+00 |  |
| EM load | D max | mm | 2.756 | w/o support block | Type C modular coil |
| ● stellalloy E=145GPa | DZ | mm | (-1.02 - 1.322) | w/o support block |  |
| ● Regular PF shim | Seqv | Pa | 4.03E+08 | PowerGraphics OFF | MCWF flange shim |
| ● PF shim COF effect | Seqv | ksi | 5.85E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 2.95E+04 |  | ALPX=9.829E-6 |
| Vertical spring support | OB reaction | kip | 6.63E+00 | Total weight |  |
| Run: em-h4a | IB reaction | N | -2.96E+04 | -1.000E+02 | SS shim on PF6 sup. |
| w/PF6 link & bonded TF shim | IB reaction | kip | -6.65E+00 | -2.248E-02 |  |
| DL, EM & Cooldown | D max | mm | 5.154 | w/o support block | Dmax at TF coil mid-plane |
| ● stellalloy E=145GPa | DZ | mm | (-1.889 - 1.252) | w/o support block | Dzmax at PF coil (near center) |
| ● Regular PF shim | Seqv | Pa | 5.01E+08 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 7.27E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 2.06E+05 |  | ALPX=9.829E-6 |
| Vertical spring support | OB reaction | kip | 4.64E+01 | Total weight |  |
| Run: h5-emdlco-2T000s | IB reaction | N | 1.51E+05 | 3.570E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.39E+01 | 8.026E+01 |  |
| *Note: model h5 running from single step file is identical to model h4 (from multi-step files) |  |  |  |  |  |
| DL, EM & Cooldown | D max | mm | 5.829 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-4.307 to -1.167) | unsel Type255-spring | Dzmax at PF coil (near center) |
| ● Regular PF shim | Seqv | Pa | 5.00E+08 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 7.25E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.90E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.28E+01 | Total weight |  |
| Run: h6-emdlco-2T-HB000s | IB reaction | N | 1.67E+05 | 3.570E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.75E+01 | 8.026E+01 |  |
| DL, EM & Cooldown | D max | mm | 6.838 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-4.330 to -1.190) | unsel Type255-spring | Dzmax at PF coil (near center) |
| ● Regular PF shim | Seqv | Pa | 4.97E+08 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 7.21E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.89E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.26E+01 | Total weight |  |
| Run: h6-emdlco-2T-HB440s | IB reaction | N | 1.67E+05 | 3.562E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.75E+01 | 8.007E+01 |  |
| DL, EM & Cooldown | D max | mm | 6.26 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-4.066 to -1.446) | unsel Type255-spring | Dzmax at PF6 coil |
| ● Regular PF shim | Seqv | Pa | 5.03E+08 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 7.30E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.89E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.25E+01 | Total weight |  |
| Run: h6-emdlco-17T-Om000s | IB reaction | N | 1.67E+05 | 3.564E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.76E+01 | 8.013E+01 |  |
| DL, EM & Cooldown | D max | mm | 5.699 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-4.154 to -1.471) | unsel Type255-spring | Dzmax at PF6 coil |
| ● Regular PF shim | Seqv | Pa | 4.90E+08 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 7.11E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.89E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.25E+01 | Total weight |  |
| Run: h6-emdlco-17T-Om440s | IB reaction | N | 1.68E+05 | 3.570E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.77E+01 | 8.027E+01 |  |
| DL, EM & Cooldown | D max | mm | 9.664 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-4.131 to -1.395) | unsel Type255-spring | Dzmax at PF6 coil |
| ● Regular PF shim | Seqv | Pa | 4.96E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 7.19E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.87E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.21E+01 | Total weight |  |
| Run: h6-emdlco-17T-iota065 | IB reaction | N | 1.66E+05 | 3.530E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.73E+01 | 7.937E+01 |  |
| DL, EM & Cooldown | D max | mm | 9.296 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-3.939 to -1.453) | unsel Type255-spring | Dzmax at PF6 coil |
| ● Regular PF shim | Seqv | Pa | 4.85E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 7.04E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.84E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.13E+01 | Total weight |  |
| Run: h6-emdlco-17T-iota019 | IB reaction | N | 1.64E+05 | 3.478E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.69E+01 | 7.819E+01 |  |
| DL, EM & Cooldown | D max | mm | 5.671 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-4..039 to -1.386) | unsel Type255-spring | Dzmax at PF6 coil |
| ● Regular PF shim | Seqv | Pa | 4.95E+08 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 7.18E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.90E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.26E+01 | Total weight |  |
| Run: h6-emdlco-17T-shear01 | IB reaction | N | 1.67E+05 | 3.570E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.76E+01 | 8.026E+01 |  |
| DL, EM & Cooldown | D max | mm | 4.86 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-3.629 to -1.978) | unsel Type255-spring | Dzmax at PF6 bracket |
| ● Regular PF shim | Seqv | Pa | 4.72E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 6.85E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | 1.80E+05 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | 4.05E+01 | Total weight |  |
| Run: h6-emdlco-05T-TF | IB reaction | N | 1.64E+05 | 3.442E+05 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 3.69E+01 | 7.739E+01 |  |
| EM & Cooldown | D max | mm | 3.976 | unsel Type255-spring | Dmax at TF coil mid-hight |
| ● stellalloy E=145GPa | DZ | mm | (-0.693 to 0.980) | unsel Type255-spring | Dzmax at PF6 bracket |
| ● Regular PF shim | Seqv | Pa | 4.64E+08 | PowerGraphics OFF | TF bracket |
| ● PF shim COF effect | Seqv | ksi | 6.73E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | -5.91E+03 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | -1.33E+00 | Total weight |  |
| Run: h6-emco-05T-TFa | IB reaction | N | -6.96E+03 | -1.287E+04 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | -1.56E+00 | -2.893E+00 |  |
| Cooldown | D max | mm | 4.667 | unsel Type255-spring | Dmax at TF coil mid-hight? |
| ● stellalloy E=145GPa | DZ | mm | (-0.820 to 0.879) | unsel Type255-spring | Dzmax at PF6 bracket? |
| ● Regular PF shim | Seqv | Pa | 4.68E+08 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 6.79E+01 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | -1.27E+03 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | -2.86E-01 | Total weight |  |
| Run: h6-co-05T-TFb | IB reaction | N | 1.27E+03 | 0.000E+00 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | 2.86E-01 | 0.000E+00 |  |
| EM Load | D max | mm | 0.708 | unsel Type255-spring | Dmax at TF coil mid-hight? |
| ● stellalloy E=145GPa | DZ | mm | (0.006 to 0.244) | unsel Type255-spring | Dzmax at PF6 bracket? |
| ● Regular PF shim | Seqv | Pa | 3.37E+07 | PowerGraphics OFF | TF bracket? |
| ● PF shim COF effect | Seqv | ksi | 4.89E+00 | PowerGraphics OFF | ALPX=9.829E-6 |
| ● TF shim COF effect | OB reaction | N | -7.18E+03 |  | ALPX=9.829E-6 |
| New support springs | OB reaction | kip | -1.61E+00 | Total weight |  |
| Run: h6-em-05T-TFc | IB reaction | N | -5.69E+03 | -1.287E+04 | SS shim on PF6 sup. |
| w/PF6 link | IB reaction | kip | -1.28E+00 | -2.893E+00 |  |

Appendix II

| FIELD PERIOD ASSY WEIGHT |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Component |  | Pro E Weight |  | contingency | Total Weight |  | delta |
|  |  | lbs | tons |  | tons |  | lbs |
| Vacuum Vessel |  | 6,776 | 3.4 | 5% | 3.6 |  | 339 |
| Modular Coils |  | 43,402 | 21.7 | 5% | 22.8 |  | 2,170 |
| TF Coils |  | 8,100 | 4.1 | 5% | 4.3 |  | 405 |
| Heating/Cooling Hdwr |  | 529 | 0.3 | 5% | 0.3 |  | 26 |
| PF Coils |  | 5,505 | 2.8 | 5% | 2.9 |  | 275 |
| PFCs & NBL-duct |  | 12,043 | 6.0 | 5% | 6.3 |  | 602 |
| Trim coils & supp'ts |  | 2,007 | 1.0 | 5% | 1.1 |  | 100 |
| PF & TF Structure & C.S. |  | 11,236 | 5.6 | 5% | 5.9 |  | 562 |
| Total Weight |  | 89,599 | 44.8 | 5% | 47.0 |  | 4,480 |
|  |  |  |  |  | 47.0 |  |  |
| Does not include |  |  |  |  |  |  |  |
|  |  | Guessed Wt. |  |  |  |  |  |
| Insulation |  | 600 |  |  |  |  |  |
| Cryostat panels & structure |  | 3,500 |  |  |  |  |  |
| Magnetic Loops |  | 100 |  |  |  |  |  |
| some of the Fastners |  | 500 |  |  |  |  |  |
| Full Period Total Wt.: |  | 94,299 |  |  |  |  |  |
| Full Period Project weight | 100,000 |  |  |  |  |  |
| (estimate for design purposes) |  |  |  |  |  |  |  |

# Text boxes

Controlled Document

THIS IS AN UNCONTROLLED DOCUMENT ONCE PRINTED.

Check the NCSX Engineering Web prior to use to assure that this document is current.

Peak Tresca Stress – 12.4 ksi

~35

Seismic Loading on Anchors:

(w/o. 12 addition anchors)

Forces on concrete wedge studs:

NODE      FX          FY          FZ

16560   398.70     -2210.4      4315.8

16612   4552.2     -3412.6     -3288.6

17234   826.51      5147.6     -1534.6

17286  -492.71      667.62      52.423

19454  -3423.9      3347.4      340.46

19467  -2536.8     -3199.8     -955.54

21988   444.46     -2947.8      674.77

22070  -136.47     -3393.3      2775.4

22698  -799.82      6116.4      1872.8

27352  -3.9376      446.26      2409.3

27434   1713.6     -1165.6      2378.7

27982   5766.0     -5069.0     -450.61

28064  -687.22      618.00     -962.14

32724  -424.18      186.34     -697.50

32806   8688.9      7165.1     -462.25

33354   7462.7      4044.8      6025.2

33436  -1419.8     -1271.9      5776.6

For minimum embedment 4.5” in 4,000 lb R.C.

Shear area of stud	.78 sq.in.

Max. Shear force	11,262 lbs (node 32806)

Max. Shear in stud	14.4 ksi

Max. pullout load	6.03 kip (node 33354)

Rated stud capacity	13,000 lbs pullout

Rated Shear cap.	22,920 lbs

Reduction for 3,000psi concrete  75%:

Stud capacity	 9,750 lbs pullout

Shear capacity	17,190 lbs

For recommended stud spacing:

Margin on shear load	1.5x

Margin on pullout	1.6x

Reduction for stud less spacing 75% of rated values:

Margin on shear	~1.1x

Margin on pullout	~1.2x

Loading & stress on the anchors for all operating conditions are substantially less (~50%) than this DBE seismic loading

~35

Fatigue Considerations:

The facility shall be designed for the following maximum number of pulses when operated per the reference scenarios defined in Section 3.2.1.5.3.3.1 and based on the factors for fatigue life specified in the

NCSX Structural and Cryogenic Design Criteria Document:

• 100 per day;

• 13,000 per year; and

• 130,000 lifetime.

Max. operational load O.B. columns:  53.9

S max = 14.2 ksi, S min = 12.0 ksi

S mean = 13.1 ksi

Seq. = 2.67 ksi

20x life = 2.6e6 cycles

---> 26 ksi limit >> max stress intensity

--->  S max < 2 x S130,000 cycles