NCSX Pumping Speed

| Note: All pumping speeds and conductances are for air and in l/s |
| --- |
| 1/CT = 1/C1 + 1/C2 +…..+ 1/Cn (for conductances and pumps in series) |
| CT = C1 + C2 +……+ Cn (for conductances and pumps in parallel) |
| Reference: A. Roth, Vacuum Technology 3rd Edition |
| Effective pumping speed of 2 TMPs in parallel to the large pumpduct |
|  | 1st pump to 24" main duct | 2nd pump up to 24” main duct |
| TMP= | 1,450 | 1,450 |
| Component | TIV | TIV |
| Conductance diameter in inches= | 10.0 | 10.0 |
| Conductance length in inches= | 5.5 | 5.5 |
| Conductance= | 14,196 | 14,196 |
| Component | Elbow and Spool Piece | Elbow and Spool Piece |
| Conductance diameter in inches= | 13.5 | 13.5 |
| Conductance length in inches= | 32.0 | 32.0 |
| Conductance= | 6,003 | 6,003 |
| Effective pumping speed of each TMP to duct= | 1,079 | 1,079 |
| Effective pumping speed of 2 TMPs in parallel to main duct (S1) = 2,158 |

| Calculation of conductances in series |
| --- |
| Component | Vertical 24" duct |
| Conductance diameter in inches= | 23.25 |
| Conductance length in inches= | 90 |
| Conductance= | 10,903 |
| Component | Transition to NB duct |
| Conductance diameter in inches= | 13.5 |
| Conductance length in inches= | 22 |
| Conductance= | 8,732 |
| Component | Vertical part of NB duct |
| Length of 1st side in inches= | 13.5 |
| Length of 2nd side in inches= | 20.0 |
| Conductance length in inches= | 17 |
| Conductance= | 29,848 |

| Component | Horizontal part of NB duct |
| --- | --- |
| Length of 1st side in inches= | 13.5 |
| Length of 2nd side in inches= | 33 |
| Conductance length in inches= | 10 |
| Conductance= | 99,522 |
| Component | NB port spool piece extension |
| Conductance diameter in inches= | 23 |
| Conductance length in inches= | 23 |
| Conductance= | 41,303 |
| Component | NB port spool piece |
| Conductance diameter in inches= | 23 |
| Conductance length in inches= | 6 |
| Conductance= | 158,330 |
| Effective conductance of components in series from 24” main duct to the VV (C1) = 3567 |

Approximate effective NCSX pumping speed {Seff=( S1* C1)/( S1+ C1)} = 1,345