# EQUIPMENT REQUIRING NCSX PORT SPACE

## Fueling

Gas Injector Assembly:

- One per period (3 total)

- Requires a 2 ¾ “ CFF

- Must be located on a high conductance port with direct line of site to the plasma but need not be centered on the port.

- If the gas injector were to be located on a reentrant port an 8” CFF would be needed.

Inboard wall Injection (gas or pellet):

- One per period (3 total); need not be located symmetrically.

- Requires a 2 ¾ “ CFF

- A ½” OD guide tube would be used to provide perpendicular plasma injection.

- To satisfy pellet injection the minimum bend radii would be 6”.

Supersonic Gas Injection:

- One per period (3 total) on outboard port; need not be located symmetrically.

- Requires a 4 5/8 “ CFF

## Vacuum Systems

Turbomolecular pump (TMP) systems:

- TMP pumping systems (2 total)

- Located on the lower (or upper) NBI port duct.

Residual Gas Analyzer (RGA):

- A residual gas analyzer (RGA) system and a couple of capacitance manometer vacuum gauges needs to be placed near one of the transition pieces between the vacuum vessel and a neutral beam box.

Ion Gage:

- One per period (3 total); need not be located symmetrically.

- Requires a 2 ¾ “ CFF

- Must be located on a high conductance port separated from gas injectors (different port) in order to provide a true measurement.

# Wall Conditioning

Glow Discharge Cleaning System:

- Anode (paddle)

  - One per period (3 total)

  - Requires a 4 5/8 “ CFF

  - Located approximately 4-6” back of the flux surface defined by the edge of the first wall limiter.

- Filament

  - One per period (3 total)

  - Requires a 2 ¾ “ CFF

  - Located in the same port with the Anode but located near the port flange.