PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #

COGNIZANT INDIVIDUAL:	Tom Brown

ECN TITLE:  Addition of bolt circle and weld note revision

ASSOCIATED ECP:  None

CC/WP/Job: 9450/1***/1803			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE184-002 | R1 | VV Support Stand Fixture Assembly Weldments |
| SE184-003 | R1 | VV Support Stand Fixture Assembly Details |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE184-002, Loc B12: Modified weld note to identify specific weld requirement and that PPPL weld procedure is only followed if fabricated in-house. SE184-003, Loc A5: Added bolt circle for attaching support axle Weldment.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #

REASON FOR CHANGE: Weld note change was made based on QA requirement to eliminate confusion with PPPL weld procedure when fabrication of a Weldment by out side vendors. A bolt circle was added to the blank-off flange cover to save time during VV FP assembly. We are assuming that the part CG will be reasonable close to the CAD model defined CG location.

ENGINEERING CHANGE PROPOSAL: DATE: 10/18/05

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER:

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN #

(Continuation Page)

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |