PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5008

COGNIZANT INDIVIDUAL: Tom Bown

ECN TITLE:  Ball Alignment Assembly, Ball and Stud Assembly

ASSOCIATED ECP:  None

CC/WP/Job: 9450 1*** 1803			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number: 1249

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| Se1851-173 | 1 | Mod Coils, Ball Align’t Assy, Outer Alignment Washer |
| Se1851-174 | 1 | Mod Coils, Ball Align’t Assy, Inner Alignment Washer |
| se1851-175 | 1 | Mod. Coils, Ball Align’t Assy, Ball and Stud Assy |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Material revised from ASTM A108 to 316 S/S in -175 Revised threaded seat to press fit with braze in -175 Increased spring pin diameter holes to .1285 (30 drill) to accommodate standard pin and revised part and insert hole size accordingly (-173, zone B8, C6, D6 and -174 zone B6, D10 and E6) Change edge radius to undercut to insure proper assembly fit-up in -173 (zone F12) and -174 (zone E9)

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5008

REASON FOR CHANGE: ASTM A108 subject to cracking if welded Revised seat to improve accuracy Pin holes were too small to accommodate standard pins. Added undercut to improve assembly fit-up

ENGINEERING CHANGE PROPOSAL: None DATE: 7/19/2005

COGNIZANT INDIVIDUAL MAKING THE CHANGE: T. Brown

RESONSIBLE LINE MANAGER: B. Nelson