Procedure EM-006, Attachment 2

| WORK REQUEST |  |
| --- | --- |
| Section A: To be completed by requestor: |  |
| REQUESTOR: Mike Viola PHONE: 3655 DATE REQUESTED: 6/2/2005 |  |
| JOB TITLE: Modular Coil installation mockup test DATE NEEDED: As soon as available |  |
| CHARGE NUMBER: 9450 1*** 1803 MATERIAL PROVIDED BY REQUESTOR: except for block | ❏ |
| TYPE OF WORK: Check One (* Requires Checked and Approved Sketches or Dwgs. or Specifications) |  |
| ❏ A. TEMPORARY, TO BE REMOVED FROM RESEARCH DEVICE BEFORE OPERATIONS◊ (NON-SAFETY). |  |
| ❏ B. *TEMPORARY, TO BE LEFT ON RESEARCH DEVICE DURING OPERATIONS. |  |
| ❏ C. *PERMANENT ITEM PLACED ON RESEARCH DEVICE. |  |
| X D. ALL OTHER ITEMS, NO SAFETY ISSUES.(◊ Note: Weld Fabrication requires Weld Engineer Signature) |  |
| ❏ E. *WORK INVOLVING SAFETY ISSUES (ie, LIFT HARDWARE, IMPACTS ENVIRON.,PERSONAL SAFETY, etc.). |  |
| ❏ ELECTRICAL X MECHANICAL ❏ MACHINIST ❏ OTHER |  |
| ❏ D-SITE WORK DCA / ECN NO: INSTALLATION PROCEDURE NO: |  |
| ❏ REQUIRES TRITIUM LINE BREAK |  |
| DESCRIPTION OF TASK: (USE SPACE BELOW) |  |
| (INCLUDE DRAWINGS, SPECS., SKETCHES, MATERIAL REQUIREMENTS AND TEST REQUIREMENTS AS APPROPRIATE) Choose ~10 ton rectangular NCSX shielding block that could provide a 3 pick point configuration (4 side pick locations would work) Move block into TFTR Test cell. Lift block and verify that CG is at physical center. Install 3 pointer holders. Measure pointer locations using Romer arm. Install test course (3 paper squiggles) Perform 2 test courses while manipulating crane and 3 chainfalls (4 men) – observed by QA and Tom Brown |  |
| ESTIMATE OF MANDAYS REQUIRED: 2-3 men 4 days then 4 men 5 days |  |
| WORK AUTHORIZED BY: Mike Viola DATE: 6/2/2005 |  |
| Section B: To be completed by Fab and Assy Shop: |  |
| ESTIMATE OF MANDAYS REQUIRED:______________ |  |
| ACCEPTED BY:_________________________________DATE:________________ |  |
| DATE WORK WAS COMPLETED: ____________________ INITIALS:_______________ |  |