Requirements for stellarator core support

A   temporary sleds to allow assembly of machine

- Radial assembly motion

- Holds up weight

- Allows “wiggle” at top to let 3 field periods hold hands without constraint

B  Permanent supports

- Holds up weight of entire stellarator core.  All magnets are supported from

- Works at low temperature

- Allows radial motion for cooldown relative to floor

- Can be added with temporary sleds in place (adjustable)

- Provides stellarator symmetric restraint of weight and seismic loads only, no EM loads through supports

  - Allowed to twist about radial, toroidal,  and vertical axes

  - Allowed to translate radially

  - 5a radial axes at vertical elevation of supports

  - Toroidal restraint is necessary

- Support 3 locations, at plane of CC joints, (near outboard foot of type C coil better than inboard)