PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5120

COGNIZANT INDIVIDUAL: Tom Brown

ECN TITLE:  VV Support Stand Lifting Fixture

ASSOCIATED ECP:  None

CC/WP/Job:9450 1*** 1803			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE184-008 | 1 | Hoist Ring Mount Lifting Assy w/ Laser Pointer |
| SE184-009 | 1 | Lifting Fixture Details |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE184-001: Update drawing views to show revision of Hoist Ring Mount Lifting Assy SE184-008: Addition of (2) filler plates, Part # SE184-009-6; corresponding increase in 3/8-16 hex head cap screws, flat washers and lock washers. SE184-009: Added sheet 3 for detail part #6.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5120

REASON FOR CHANGE: Additional Filler plates required to prevent failure of 3/8-16 hex head cap screws under lifting load when oriented in an off axis position.

ENGINEERING CHANGE PROPOSAL: DATE:

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER: