NCSX

Design Basis Analysis

Analysis of the Modular Coil Winding Form Assembly Fixture

NCSX-CALC186-002-00

# Draft A

18 September 2006

Prepared by:

_______________________________________

Fred Dahlgren, PPPL

I have reviewed this calculation and, to my professional satisfaction, it is properly performed and correct.  I concur with analysis methodology and inputs and with the reasonableness of the results and their interpretation.

Reviewed by:

_______________________________________

Tom Brown,PPPL

Analysis of the MCWF Frame Assembly Fixture

Executive Summary:

A stress analysis of the MCWF assembly support frame was performed to assess the adequacy of the design for two (A-A) & three (A-B-C) module sub-assembly loading in the 20 and 40 degree positions which were deemed the most severe loading conditions. The loading of the frame tends to be more uniform in the 20 degree position. The loading results from the A-B-C sub-assembly in the 40 degree position resulted in 14.1ksi Tresca stress. The peak stress for the 20 degree A-B-C load was the highest overall with a peak Tresca stress of 18.1 ksi. Deflections of the frame were greatest at the center of the lower cross member of the pivoting frame section for the 40 degree position with a maximum displacement of 0.028” (for the revised 0.5” thick box section). For the 20 degree position (w/revised lower cross beam) the maximum deflection occurs in the mounting gussets and peaks at 0.034” in the upper corner gussets. The peak Tresca stresses for the 20 degree position A-B-C assembly occur at the mounting bolt perimeters of the corner gussets and at the stanchion pivot pin hole perimeters, but do not exceed the allowable 24 ksi stress for A36 steel (assuming a 2/3rd yield allowable criteria).

Analysis Methodology:

The analysis was performed using MSC/Nastran, a general purpose finite element analysis computer program. The FEA model was generated from the dimensional information contained in the Pro-E CAD models referenced below. The centers of gravity were located from the Pro-E model SE185-113 for the various sub-assemblies and frame positions. A review of the various sub-assembly configurations revealed that the section A-A & A-B-C combinations produced the most severe loading conditions and there were therefore selected for the 20 & 40 degree analysis. In all four separate models were run. The database and Nastran input files are referenced below.

Project Reference Documents:

Pro-E models/drawings:

SE185-111

SE185-112

SE185-113

SE185-116

SE185-118

Nastran FEA Models:

FEA Database		Nastran Input file

mcwf-frame20a.db 		mcwf-frame20a.bdf

mcwf-frame20abc.db		mcwf-frame20abc.bdf

mcwf-frame40a.db - 		mcwf-frame40a.bdf

mcwf-frame40abc.db - 	mcwf-frame40abc.bdf

Modular Coil Winding Form Frame Assembly Fixture Analysis

Introduction:

A structural FE analysis was performed to determine the adequacy of the Modular Coil Winding Form (MCWF) Frame Assembly fixture design. The assembly fixture is a weldment comprised of several standard 6” x 6” x 3/8th thick A36 box beam sections for the base with  ½” thick welded stanchions (“sandwich plates” per dwg. SE185-113) and two pivot frame weldments. The ½” thick stanchions on the base frame accommodate and support the articulating pivot frame members attached with removable pivot pins. These pivot frames support one, two, or three Modular Coil/shell segments oriented at either 20 or 40 degrees from the horizontal plane. The full frame assembly is shown in Figure 1 in the 40 degree configuration, and in figure 2 with the pivot frame in the 20 degree position.

Figure 1. MCWF Frame Assembly Fixture (Shown in the 40 degree position)

Assumptions:

The analysis assumes that the MCWF segments are stiff enough (relative to the frame structure) that they can be adequately represented by rigid elements attached to the C.G. as defined by the Pro-E models referenced above, and that the loads are properly distributed to the mounting points on the frame by this mechanism. It also assumes that the frame attaches to a floor which is an infinitely rigid structure.

FEA Model Description:

The frame box sections are modeled with simple quadrilateral and triangular plate elements (CQUAD4/CTRIA3-Nastran plate elements) with both bending and membrane stiffness. To avoid having to model the complex Modular Coil with the winding form, it was represented by four rigid elements ( shown in figures 1 & 2 as magenta lines), attached to the articulating frame at the four bolted attachment points and at the acting center of gravity of  the MCWF assembly. The rigid elements imply an infinitely stiff MCWF structure which (when compared to the supporting frame assembly) is a reasonable approximation. The frame itself is constrained in the vertical direction at the lower nodes of the base frame and at the centers of the welded angle hold-downs which are also constrained in the other 5 DOFs, representing an anchor bolt attachment to a rigid concrete floor. The pivot pin attachments are represented by multipoint constraints (MPCs in Nastran), which structurally tie the pivot frame pin hole perimeters to the hole perimeters of the stanchions (the pins are therefore also assumed to be infinitely stiff relative to the frame members). The loading for the maximum A-A MCWF segments of 12,266 lbs was applied vertically down at the grid point representing the C.G. of the A-A assembly and connected to the four rigid elements. The most extreme loading is the A-B-C sub-assembly which weighs 18,271 lbs.

Figure 2. MCWF Frame Assembly Fixture (Shown in the 20 degree position)

Discussion and Results:

20 Degree Position:

Results for the A-A assembly load case are shown in figures 3 and 4. the maximum displacements of 0.027”  occur at the lower cross beam and corner brackets . The peak Tresca stress is 13.7 ksi  at the lower support pin hole perimeters in the base frame stanchions. Note these results were from the model with the 3/8” thick wall lower cross beam.

Figure 3 Displacements (SRSS) for A-A loading in 20-degree position

Figure 4. Tresca stress contours for A-A assembly loads @ 20 degrees

The displacement contours for the A-B-C assembly in the 20-degree position are shown in figure 5. The peak (SRSS) displacement is 0.034” at the upper corner gussets . The Tresca stress contours for this load case are shown in figure 6a. The peak stress of 18.1 ksi is at the stanchion pin hole perimeters. Note these model results include the thicker (0.5” thick) lower cross beam. Figure 6b shows the peak Tresca stress in the pin is at 21.9 ksi although this is likely an overly high result due to model limitations. Note that the red color of the plate elements representing the box frame and stanchions is just the default fill color when plotting the solid element pin stresses using the Patran post processor.

Figure 5. Displacement contours for A-B-C                  		20 degree loading

Figure 6a. Tresca stress contours for A-B-C

20 degree loading

Figure 6b. Tresca stress contours in the support pin for the A-B-C 20-degree loading

40-Degree position:

It was determined that the A-A sub-assembly, with winding forms, shims, bolts, and coils, was the largest loading for a two segment setup, with a load of 12,266 lbs. acting at the C.G.s shown in figures 1 & 2. The peak load estimated for a full A-B-C half-period sub-assembly was 18,271 lbs. The C.G.s for this configuration are shown in figure 7. Figure  8 shows the various thicknesses of the final structure.

Figure 7. FEA model of the MCWF support frame at the 40-degree angle for ABC

Figure 8. A contour plot of the thickness for various members of the frame

Figure 9. Displacements (SRSS) for the A-A assembly loading at 40 degrees.

Displacement contours for the A-A assembly are shown in figure 9 above. The maximum deflection of the frame occurs at the lower cross brace and is seen to be 0.025” The contours of the Tresca stress are shown below in figure 10. The peak stress in the frame is 17.4 ksi peaking at the lower stanchions (item 10 “sandwich” plates on SE185-113) . The allowable stress for A36 using a 2/3rd yield criteria is 24 ksi.

Figure 10. Tresca stress contours on Z1 surface for the A-A segment load

Figure 11. Tresca stress contour – Z1 surface for A-A segment loading – Peak stress @ pinned joint 		    stanchions

Initial analysis of the A-B-C sub-assembly shown in figure 6 in the 40-degree position yielded fairly high stresses in the lower cross member of the pivot frame. Maximum displacement of the frame was just over 0.034” at the cross member center. Due to flexing of the cross member the lateral box sections experience torsional flexing which tended to put higher stresses (from bending) into the pinned joint and stanchions. To alleviate this condition a heavier wall box section (0.5” vs. 0.375”), for the lower cross member has been recommended. Figure 8 above shows the thicker section. Displacement results with the thinner and thicker cross member are shown in figures 12 & 13 below. Figure 12 is a contour plot of the displacement for the thinner cross member indicating a peak of 0.034” an the center of the cross member. Figure 13  shows a peak displacement of  0.028” with the heavier wall.

Figure 12 Displacements (SRSS)  0.375 thick wall   Figure 13 Displacements (SRSS) – 0.500” thick wall

Figure 14 shows the Tresca stress contours for the 40-degree A-B-C MCWF subassembly with the thicker (0.500”) lower cross member. The peak stress is 14.1 ksi at the upper corner gussets and at the stanchion around the mounting bolt hole perimeters. Figures 15 & 16 show the Tresca stress contours at these locations. The peak stress in the lower cross brace is 7.5 ksi at the lower mounting  bolt hole perimeters.

Figure 14. Tresca stress contours for the 40-degree A-B-C MCWF sub-assembly (18,271 lb. load)

Figure 15 Tresca stress contours @ stanchion &  cross member

Figure 16 Tresca stress contours @ upper gusset

Conclusions:

A stress analysis of the MCWF assembly support frame was performed to assess the adequacy of the design for two (A-A) & three (A-B-C) module sub-assembly loadings in the 20 and 40 degree positions which were deemed the most severe loading conditions. The loading of the frame tends to be more uniform in the 20 degree position. The loading results from the A-B-C sub-assembly in the 40 degree position resulted in 14.1ksi Tresca stress. The peak stress for the 20 degree A-B-C load was the highest overall with a peak Tresca stress of 18.1 ksi. Deflections of the frame were greatest at the center of the lower cross member of the pivoting frame section for the 40 degree position with a maximum displacement of 0.028” (for the revised 0.5” thick box section). For the 20 degree position (w/revised lower cross beam) the maximum deflection occurs in the mounting gussets and peaks at 0.034” in the upper corner gussets. The peak Tresca stresses for the 20 degree position A-B-C assembly occur at the mounting bolt perimeters of the corner gussets and at the stanchion pivot pin hole perimeters, but do not exceed the allowable 24 ksi stress for A36 steel (assuming a 2/3rd yield allowable criteria).

# Text boxes

12,266 lbs Acting @ the A-A sub-ass’y.C.G

12,266 lbs Acting @ the A-A sub-ass’y.C.G

12,266 lbs Acting @ the A-A sub-ass’y.C.G.

Four rigid elements representing the MCWF (as infinitely stiff).

Yellow areas are 0.5” thick & Green areas are .375” thick.

Four rigid elements represent the MCWF as an infinitely stiff structure

Peak Tresca stress @ bolt perimeters 14.1 ksi

Controlled Document

THIS IS AN UNCONTROLLED DOCUMENT ONCE PRINTED.

Check the NCSX Engineering Web prior to use to assure that this document is current.