PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5185R1

# COGNIZANT INDIVIDUAL:	David Williamson

# ECN TITLE:	Flange Hole Counterbore Clearance Envelope and Type-B Post Mod

# CC/WP/Job:	9450-1***-1411	                          AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE141-114 | 8 | Type-A Modular Coil Winding Form |
| SE141-115 | 9 | Type-B Modular Coil Winding Form |
| SE141-116 | 8 | Type-C Modular Coil Winding Form |
| Continued on the Back |

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN # 5185R1

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments) SE141-114, Added note 17 “SEE DRAWING SE141-114G FOR ADDITIONAL CLEARANCE REQUIREMENTS ON ALL FLANGE BACK SPOT FACES”. SE141-115, Added note 17 “SEE DRAWING SE141-115G FOR ADDITIONAL CLEARANCE REQUIREMENTS ON ALL FLANGE BACK SPOT FACES”. SE141-116, Added note 17 “SEE DRAWING SE141-116G FOR ADDITIONAL CLEARANCE REQUIREMENTS ON ALL FLANGE BACK SPOT FACES”. SE141-115, Sht-7, Quad-B4 - For Type-B MCWF, a clearance dimension of 9.00 +/-.05-in is defined between the center of the lead block mounting pad and the support post. Clearance envelope height extends through the post as required. SE 141-115, ADDED NOTE 18 “SHEET 3, ZN B7, OFFSET THE HOLE PATTERN IN THE VACUUM VESSEL SUPPORT BOSSES RELATIVE TO THE CAST PADS AS NECESSARY TO PERMIT MORE (OR ALL) OF THE TAPPED HOLES IN THE PADS TO BE PROVIDED. NCSX WILL WELD MOUNTING STUDS AS NEEDED. SEE RFD-14-023R1 FOR ADDITIONAL INFORMATION. SE 141-116, ADDED NOTE 18 “SEE DRAWING SE141-148 FOR HOLE LOCATION AND SIZE.” (SHEET 5, ZN E6) REASON FOR CHANGE: The CAD model of the counterbore envelope, 3-in dia x 3-in length with a spherical radius, is not large enough to provide adequate fastener clearance in heavy stocked areas of the casting. There is approx .5-in stock on all sides of the B1 and B2 support posts, which prevents mounting of the leads terminal asm.

ENGINEERING CHANGE NOTICE APPROVALS: DATE: 11/07/2006

COGNIZANT INDIVIDUAL MAKING CHANGE:

DESIGN RESPONSIBLE LINE MANAGER:

MANUFACTURING RESPONSIBLE LINE MANAGER: