Major Tool & Machine, Inc.

Page: 1

1458 East 19th Street

MTM N/C: 19562

Date: 04/07/06

Indianapolis, IN 46218-4289

User ID: MCCORKLE

PRINCETON PLASMA PHYSICS LAB

Customer:

Telephone:

609-243-3655

Contact:

Mike Viola

mviola@pppl.gov

E-Mail:

609-243-2021

Fax:

S005243-F/Ln:2

Customer P.O.:

/

Part:

VVSA 2

Serial No.:

2

Revision:

SE120-004

Drawing ID:

317-636-6433

Telephone:

DOUG MCCORKLE

Reported By:

Fax:

317-634-9420

E-Mail:

dMcCorkle@MajorTool.com

Problem:

THE RESULT OF PROFILE DEVIATION ON THE VESSEL ENDS CAUSES A MIS-ALIGNMENT TO THE

VESSEL FLANGES.  REFER TO PHOTOS FOR ADDITIONAL DESCRIPTION.

Proposed Disposition:

CUSTOMER DISPOSITION REQUIRED

RECOMMEND LEAVING THE VESSEL WALL IN ITS CURRENT POSITION AND ALTERING THE WELD

SCHEME TO BLEND THE TWO SURFACES TOGETHER IF NO ASSEMBLY OR PLASMA INTERFERENCE

EXIST.

0

Number of additional pages:

Customer Disposition:       [   ] Use As Is          [  ] Rework          [  ] Repair          [  ] Scrap          [  ] Replace

Date:

Title:

Technical Contact Approval:

Date:

Title:

Buyer Approval:

Title:

Date:

Major Tool Implemented By:

/Open

n:\mtmapps\Mtnonc14.qrp

Major Tool and Machine, Inc.  1458 East 19th Street, Indianapolis, IN 46218-4289  Tel: 317-636-6433  Fax: 317-634-9420

Nonconformance Report: Major Tool NC19562

This is for SE120-004   VVSA #2 end flange fit up and weld.

Problem:

THE RESULT OF PROFILE DEVIATION ON THE VESSEL ENDS CAUSES A MIS-ALIGNMENT TO THE

VESSEL FLANGES.  REFER TO PHOTOS FOR ADDITIONAL DESCRIPTION.

MTM Recommended Disposition:

RECOMMEND LEAVING THE VESSEL WALL IN ITS CURRENT POSITION AND ALTERING THE WELD

SCHEME TO BLEND THE TWO SURFACES TOGETHER IF NO ASSEMBLY OR PLASMA INTERFERENCE

EXIST

See pictures below:

8 O’clock Inside of Flange B				8 O’clock Inside of Flange B

2 O’clock Outside of Flange B

8 O’Clock Inside of Flange A (nearly flush) 			10 O’clock outside of Flange A

Project Disposition:

Rework as Recommended by MTM.

Ensure weld size is equal or greater to original.

Approvals:

___________________________________________

Procurement Technical Representative

___________________________________________

Art Brooks, Technical Assurance

____________________________________________

Responsible Line Manager:

____________________________________________

Project Quality Assurance: