| IDC # 70 : : {g¦.5¦A¦B¦C}: REFERENCE IGES INFORMATION | 1 F3 | A(ccepted) on IDC |
| --- | --- | --- |
| IDC # 90 : : 2X.03X45° | 2 G8 | Not on NC18297 Although not chamfered, MTM says this edge is broken |
| IDC # 140 : P TO M: {g¦.1¦R¦S¦T}: REFERENCE IGES INFORMATION | 2 G6 | This is insufficient Tee base for shooting studs. Must be correct on future castings |
| IDC # 160 : Q TO N: {g¦.1¦R¦S¦T}: REFERENCE IGES INFORMATION | 2 G3 | This is insufficient Tee base for shooting studs. Must be correct on future castings |
| IDC # 180 : M TO N: {g¦.02¦R¦S¦T}: REFERENCE IGES INFORMATION | 2 F5 |  |
| IDC # 190 rejected: : 8X 3 - .626 Ø.375-16 UNC .188 DEEP C'BORE Ø.625 | 2 C5 | Not on NC18297 |
| IDC # 210 rejected: : 96X 3 - .Ø1-8 UNC .THRU | 3 G7 | Not on NC18297 |
| IDC # 230 rejected: : {f¦.01} | 3 H3 | Not on NC18297 |
| IDC # 250 : : {f¦.01}: .032 | 3 F3 | Kevin was to check on the 0.032’ as it looked high compared to the IGES data. |
| IDC # 260 : : R76.00: REFERENCE IGES INFORMATION | 3 F5 |  |
| IDC # 270 : : R73.70: REFERENCE IGES INFORMATION | 3 E5 |  |
| IDC # 280 : 8X Ø1.13 THRU BACK SPOT FACE Ø2.38 MIN DEPTH FOR C'UP: {#¦.01¦A¦B¦C}: .010 - .031 | 3 E4 |  |
| IDC # 290 : 3X Ø1.88 THRU Ø3.00 BACK SPOTFACE MIN TO CLEANUP:{#¦.010¦D¦A¦N}: .0304 - .0442 , >3.00 SPOT, 1.87 - 1.88 DIA. | 4 H8 |  |
| IDC # 300 : 3X SPH R.75 TO .75 DEEP: {#¦d.01¦D¦A¦N}: .019 - .020 , R .74 - .745 | 4 H7 | Spherical alignment features Must be improved on future castings |
| IDC # 310 : 17X Ø1.88 THRU Ø3.00 BACK SPOTFACE MIN TO CLEANUP:{#¦d.01¦D¦A¦N}: .009 - .059, >3.00 SPOT, 1.87 - 1.88 | 4 H6 |  |
| IDC # 320 : 3X Ø1.13Ø2.38 BACK SPOTFACEMIN TO CLEANUP: {#¦d.01¦D¦A¦N}: .047 - .054, 1.126 - 1.127 | 4 H5 |  |
| IDC # 340 : 3X Ø1.375-6 UNC THRU: {#¦d.01¦D¦A¦N}: .022 - .039 | 4 E6 |  |
| IDC # 350 : 5X Ø1.88 THRU Ø3.00 BACK SPOTFACE MIN TO CLEANUP:{#¦d.01¦D¦A¦N}: .0019 - .0182, >3.00 SPOT | 4 E6 |  |
| IDC # 360 : Ø1.88 THRU Ø3.00 BACK SPOTFACE MIN TO CLEANUP: {#¦d.01¦D¦A¦N}:.018, >3.00 SPOT, 1.879 DIA. | 4 D4 |  |
| IDC # 380 : Ø1.88 THRU Ø3.00 BACK SPOTFACE MIN TO CLEANUP: {#¦d.01¦E¦A¦J}:0.77, >3.00 SPOT. | 5 E8 | Flange bolt hole placed per Rev. 4 rather than Rev. 6 |
| IDC # 410 : 3X SPH R.75 TO .75 DEEP: {#¦d.01¦E¦A¦J}: .020 - .021 | 5 F6 |  |
| IDC # 430 : 24X Ø1.88 THRU Ø3.00 BACK SPOTFACE MIN TO CLEANUP:{#¦d.01¦E¦A¦J}: .008 - .040, >3.00 SPOT. | 5 E7 |  |
| IDC # 440 : 3X Ø1.5 TO 2.00 DEEP Ø3.00 TO 1.00 DEEP: {#¦d.01¦E¦A¦J}: .013 - .037 | 5 E7 |  |
| IDC # 510 – 540 Poloidal Break features |  | Not Inspected – Included on NC118315 listing areas without inspection results. This includes the flanges which are 0.5” undersized. Must be inspected on future castings (MTM has already orally acknowledged this) |
| IDC # 550 : : R7.00: REFERENCE IGES INFORMATION | 7 G2 |  |
| IDC # 560 : : 2X R1.50: REFERENCE IGES INFORMATION | 7 F2 |  |
| IDC # 580 : : 90`: 87.92 | 7 E2 |  |
| IDC # 610 : : 6.50 ~ .010: 6.486 | 7 E2 |  |
| IDC # 620 : : 3.06 ~ .010: REFERENCE IGES INFORMATION | 7 E2 | Included on NC118315 listing areas without inspection results |
| IDC # 630 : : R4.00 ~ .010: REFERENCE IGES INFORMATION | 7 D2 | Included on NC118315 listing areas without inspection results |
| IDC # 640 : : 2.10 ~ .010: REFERENCE IGES INFORMATION | 7 D3 | Included on NC118315 listing areas without inspection results |
| IDC # 650 : : 4.00 ~ .010: 3.98 | 8 G7 |  |
| IDC # 670 : : R4.00 ~ .010: REFERENCE IGES INFORMATION | 8 G7 | Included on NC118315 listing areas without inspection results |
| IDC # 690 : : 9.38 ~ .010: REFERENCE IGES INFORMATION | 8 E3 | Included on NC118315 listing areas without inspection results |
| IDC # 700 : : 6.0`: REFERENCE IGES INFORMATION | 8 E2 | Included on NC118315 listing areas without inspection results |
| IDC # 710 : : d8.00 ~ .010: REFERENCE IGES INFORMATION | 8 C2 | Included on NC118315 listing areas without inspection results |
| IDC # 720 : : 5.9`: REFERENCE IGES INFORMATION | 8 B3 | Included on NC118315 listing areas without inspection results |
| IDC # 730 : : 7.81 ~ .010: REFERENCE IGES INFORMATION | 8 B3 | Included on NC118315 listing areas without inspection results |
| IDC # 740 : : 7.25 ~ .010: REFERENCE IGES INFORMATION | 8 C6 | Included on NC118315 listing areas without inspection results |
| IDC # 750 : : 6X d..375-16 UNC TO .75 DEEP.03 X 45` CHAMFER: ACCEPT THREAD/CHAMFER, .53 - 1.32 DEPTH | 8 D7 |  |
| IDC # 780 : : 2.19 ~ .010: 2.172 - 2.198 | 8 D7 |  |
| IDC # 790 : : 2.19 ~ .010: 2.176 - 2.191 | 8 D7 |  |
| IDC # 830 : : 2X 1.56 ~ .010 THRU: 1.) 1.56 2.) 1.79 | 8 C8 | Lead Block area |
| IDC # 840 : : 3.75 ~ .010: 3.90 | 8 C8 | Lead Block area |
| IDC # 850 : : 2X 7.50 ~ .010 THRU: 1.) 7.53 2.) 7.63 | 8 C8 | Lead Block area |
| IDC # 860 : : 8X R.25: .25 - .28 | 8 C8 | Lead Block area |
| IDC # 870 : : 2X 2.52 ~ .010: 2.04 - 2.08 , 2.65 - 2.66 | 8 C8 | Lead Block area |
| IDC # 900 : : 2.54 ~ .010: REFERENCE IGES INFORMATION | 9 E7 | Included on NC118315 listing areas without inspection results |
| IDC # 910 : : 5.08 ~ .010: REFERENCE IGES INFORMATION | 9 E7 | Included on NC118315 listing areas without inspection results |
| IDC # 940 : : 2.44 ~ .010: REFERENCE IGES INFORMATION | 9 E3 | Included on NC118315 listing areas without inspection results |
| IDC # 950 : : 1.22 ~ .010: REFERENCE IGES INFORMATION | 9 E3 | Included on NC118315 listing areas without inspection results |
| IDC # 980 : : {g¦.125¦A¦B¦C}: REFERENCE IGES INFORMATION | 10 C8 |  |
| IDC # 990 : : {g¦.5¦A¦B¦C}: REFERENCE IGES INFORMATION | 10 C8 |  |
| IDC # 1000 rejected: : {g¦.02¦R¦T¦S}: REFERENCE IGES INFORMATION | 10 C5 |  |
| IDC # 1010 rejected: : {g¦.125¦A¦B¦C}: REFERENCE IGES INFORMATION | 10 C4 |  |
| IDC # 1020 rejected: : {g¦.02¦R¦T¦S}: REFERENCE IGES INFORMATION | 10 G1 |  |
| IDC # 1030 rejected: : {g¦.5¦A¦B¦C}: REFERENCE IGES INFORMATION | 10 E1 |  |
| IDC # 1040 rejected: UOS ALL MACHINED SURFACES TO BE 250 RMS SURFACE FINISHRECORD RANGE: : 31 - 500 |  | Surface Finish Must be closer to 250 RMS on future castings |
| IDC # 1060 rejected: : 22.13 ~ .010: TAP | 4 H7 | TAP prevented CMM measurement |
| IDC # 1070 rejected: : 47.79 ~ .010: 47.76 | 4 H7 |  |
| IDC # 1080 rejected: : 59.18 ~ .010: 59.16 | 4 H6 |  |
| IDC # 1090 rejected: : 73.27 ~ .010: TAP | 4 H6 | TAP prevented CMM measurement |
| IDC # 1100 rejected: : 80.49: 80.46 | 4 H5 |  |
| IDC # 1110 rejected: : 87.87 ~ .010: 87.84 | 4 H5 |  |
| IDC # 1130 rejected: : 31.83 ~ .010: TAP | 4 G4 | TAP prevented CMM measurement |
| IDC # 1150 rejected: : 11.48 ~ .010: 11.46 | 4 F4 |  |
| IDC # 1240 rejected: : 28.17 ~ .010: TAP | 4 F8 | TAP prevented CMM measurement |
| IDC # 1270 rejected: : 43.42 ~ .010: TAP | 4 G8 | TAP prevented CMM measurement |
| IDC # 1300 rejected: : 86.42 ~ .010: 86.40 | 5 H7 |  |
| IDC # 1320 rejected: : 28.71 ~ .010: 28.69 | 5 H5 |  |
| IDC # 1390 rejected: : 4.91 ~ .010: 4.88 | 5 E8 |  |
| IDC # 1410 rejected: : 2.1`: REFERENCE IGES INFORMATION | 7 D4 |  |
| IDC # 1420 rejected: : 2.63 ~ .010: 2.63 - 2.65 | 8 D8 |  |
| Web holes misnumbered |  | Not identified by MTM |
| Poloidal Break Shim does not conform to model |  | Not identified by MTM |

Other Issues:

New Washer/Bearing Plate for Poloidal Break – new scope for MTM

Female Wing Grinding – new scope for MTM

Large Flange Counterbore/Thru Hole interference – NCR or design change?

Back spot facing of flange holes – NCR or design change?

Cooling Tube holes (enlarge all and move 2) – ECN & drawing change