NCSX

Product Specification

For The Station Two Assembly

NCSX-CSPEC-185-02-00

March 2007

Prepared by: __________________________________________________________________________

A. Lumsdaine/M. Cole

Concur: ______________________________________________________________________________

D. Williamson, Modular Coil system (WBS 14) Manager

Concur: ______________________________________________________________________________

T. Brown,  Design Integration

Concur: ______________________________________________________________________________

L. Dudek, RLM for Modular Coil Fabrication

Concur: ______________________________________________________________________________

M. Viola, ATI for Modular Coil Fabrication

Concur: ______________________________________________________________________________

J. Malsbury, Quality Assurance

Concur: ______________________________________________________________________________

J. Levine, ES&H

Approved by: _________________________________________________________________________

Phil Heitzenroeder, Engineering Manager

Record of Revisions

| Revision | Date | ECP | Description of Change |
| --- | --- | --- | --- |
| Rev. 0 | 03/5/8 | --- | Initial Release |

Table of Contents

1	OVERVIEW AND Scope	3

1.1	Overview	3

1.2	Scope	3

2	Applicable Documents	3

2.1	NCSX Documents	3

2.2	Drawings	3

2.3	Other Documents	3

3	Requirements	3

3.1	Item Definition	3

3.2	Performance	3

3.2.1	Performance	3

3.2.1.1	Coil Positioning	3

3.2.1.2	Electrical Isolation	3

3.2.2	Physical Characteristics	3

3.2.2.1	Bolted Joints	3

3.2.2.1.1	Stud Engagement	3

3.3	Error! Not a valid bookmark self-reference.Construction	3

3.3.1	Bolted Joints	Error! Bookmark not defined.

3.3.1.1	Stud Placement	Error! Bookmark not defined.

3.3.1.2	Stud Pre-Tension	Error! Bookmark not defined.

3.3.1.3	Shim Friction	Error! Bookmark not defined.

3.3.1.4	Shim Length	Error! Bookmark not defined.

3.3.2	Wing Bladder	Error! Bookmark not defined.

3.3.3	Interchangeability	3

4	Quality Assurance Provisions	3

4.1	General	3

4.2	Quality Conformance	3

4.2.1	Verification of Physical Characteristics	3

4.2.1.1	Verification of Magnetic Center	3

4.2.1.2	Verification of Electrical Isolation	3

4.2.1.3	Verification of Magnetic Permeability	3

4.2.2	Verification of Construction	Error! Bookmark not defined.

4.2.2.1	Verification of Stud Placement	3

4.2.2.2	Verification of Stud Pre-Tension	3

4.2.2.3	Verification of Shim Friction	3

4.2.2.4	Verification of Shim Length	3

4.2.2.5	Verification of Shim Welding	3

Table of Figures

Figure 1 Modular Coil Half-Period Assembly	3

Figure 2 Type-C Coil	3

# OVERVIEW AND Scope

## Overview

The assembly of the NCSX machine is accomplished at 5 stations. Stations 1 – 3 occur in the NCSX Manufacturing Facility and Station 5 and 6 occur in the NCSX Test Cell.  Station 4 activities have now been combined into Station 5.

This document details the specifications for a half-period modular coil assembly for the National Compact Stellarator Experiment (NCSX).  The Modular Coil System consists of eighteen (18) modular coils of three (3) types, designated as Type-A, Type-B, and Type-C (each shown in Figure 1 below).  The half-period (station two) assembly consists of the attachment of a Type-A coil to a Type-B coil, and the Type-B coil to a Type-C coil (for an A-B-C sub-assembly).  The NCSX machine assembly sequence can be summarized as follows (refer to the Assembly Sequence Plan, AssySeqPlan_R9.4, for more details):

- Station One – Assembly of the Vacuum Vessel assemblies (covered in NCSX-185-01)

- Station Two Assembly – half-period assembly (as detailed above) of Type-A, B, and C coils.

- Station Three Assembly – two half period assemblies assembled over the vacuum vessel.

- Station Four Assembly – not used.

- Station 5 – final full period assembly completes the FPA assembly process by bringing together a period consisting of the VVSA and two MCHP (Modular Coil Half Period) and attaching VV ports, the external trim coils, modular coil lead and coolant connections, and 4 of the 6 TF coils per period.

- Station Six Assembly – full machine assembly, joining three full periods.  This also includes the PF coils.

## Scope

This station two specification defines the product requirements for the Modular Coil Half-Period, MCHP, assembly.

Figure 1 Modular Coil Half-Period Assembly

# Applicable Documents

## NCSX Documents

[1] NCSX-ASPEC-GRD, NCSX General Requirements,  This document is referred to herein as the GRD.

[2] NCSX-CSPEC-142-05-01, Product Specification for the Modular Coil Assemblies (Type-A,B,C)

NCSX-BSPEC-14-01, System Requirements Document (SRD) for the Modular Coil System

NCSX-CRIT-BOLT-00, Handbook for Bolted Joint Design

NCSX-CRIT-CRYO-00, NCSX Structural Design Criteria

NCSX-CALC-14-001-001, Nonlinear Analysis of Modular Coil and Shell Structure

AssySeqPlan_R9.4

## Drawings

Dwg No.	Title	Rev

SE140-003	1/2 FIELD PERIOD ASSY	0

SE140-101	MCWF TYPE A	0

SE140-102	MCWF TYPE B	0

SE140-103	MCWF TYPE C	0

SE140-046	MOD COIL SHIM AND SHEAR PLATE LAYOUT	0

SE140-190	MCWF FLANGE STUD KITS	3

## Other Documents

ENG-037, PPPL WELD PROCEDURE

AWS D1.1, American Weld Specification

Assembly Sequence Plan R9.4

# Requirements

## Item Definition

Modular Coil Flange.  The Modular Coil Flanges are ridges on each edge of the coil for that are matched together to attach adjacent coils (Type-A to Type-B, and Type-B to Type-C for the station two assembly).  Flange holes match up between adjoining flanges, and are either countersunk or tapped.

Shims.  Shims of various thickness are placed between adjacent Modular Coil Flanges, and serve to position coils properly, transfer shear loads between flanges, and electrically isolate adjacent coils.  Two types of shims are utilized: a) single hole shims (coated with high friction alumina) that have a pre-tensioned flange stud going through the hole, and b) welded shims that are placed on the inboard of the coil and welded in place.

Wings.  The wing region of the modular coils is the region of the winding form that extends beyond the Modular Coil Flange (as shown below in the upper right hand of Figure 3-1 for the Type-C coil).

Wing Support Bladders.  Wing support bladders are placed between the wing of one coil and the overlapping region of the adjacent coil.  The bladders are made of Teflon and filled with glass cloth and epoxy impregnated.  They provide support for the wing region and transfer load between the wind and the adjacent coil.

Flange Studs.  Flange studs are used for attaching modular coils together at the coil flanges.  Flange studs exist in two types – tapped studs and through studs.  A large pre-tension is applied to the studs in order to transfer transverse magnetic loading to the shims (and preventing studs from incurring shear or bending loads).  The pre-tension is applied by a supernut torqued onto a series of washers, sleeves, and bushings.

Figure 3-1 Type-C Coil

## Performance

### Performance

#### Coil Positioning

The current centers of the Type B and Type C coils within a MCHP assembly must be located within +/-0.020in of the desired “best fit” location relative to the Type A coil as determined by analysis of the as-built coil geometries.

#### Electrical Isolation

Bolted joints shall electrically isolate adjacent modular coils within a MCHP assembly.  (It is recognized that the welded shims joining adjacent modular coils will indeed provide a conducting path between adjacent modular coils.)

There shall be no continuous electrical paths poloidally within a MCHP assembly.

Electrical requirements in the Modular Coil Assembly product specification [2] shall not be compromised during assembly of MCHP assemblies.

### Physical Characteristics

#### Bolted Joints

##### Stud Engagement

Studs must be threaded deeply enough in the tapped holes and nuts to carry the tensile load.

##### Stud Pre-tension

The studs will be pre-loaded to 72,000 pounds force ±1000 pounds force.

##### Shim Length

Background

Single hole shims have two notched regions so that they may be easily cut to fit flange areas with a shorter width.  If the shim overhangs the flange, it could interfere with the coil winding form or wings.  If the shim is cut too short, then it includes less surface area than possible, and could result in transverse loads being applied to the stud.

Requirement

The shim must not extend beyond the flange in such a way that it will interfere with the winding form or wings of the adjacent coil.  The shim must be within 0.62in from the end of the flange.

##### Welded Joints

Background

Two 0.44in welds will be applied to inboard shims – a weld on the inboard side of one flange and on the outboard side of the adjoining flange.

Requirement

Welds shall be completed in accordance with PPPL procedure ENG-037.  Deflections produced by the welding must not exceed the requirements of 3.2.1.1 above.

## Design and Construction

### Production Drawings

MCHP assemblies shall be assembled in accordance with the production drawings shown in Section 2.2.

### Interchangeability

Design tolerances shall permit Assemblies of the same part number to be used as replacement parts without degrading the specified performance of the parent item.  [Ref. SRD Section 3.3.5 Interchangeability]

### Magnetic Permeability

The magnetic permeability of all components and welded areas must be less than 1.02 unless otherwise authorized by the project.

### Labels

Each MCHP shall be uniquely identified as shown in Table 1.

Comment on above picture – Is there another row missing (C5/B5/A5 and A6/B6/C6)?

### Interchangeability

Design tolerances shall permit Assemblies of the same part number to be used as replacement parts without degrading the specified performance of the parent item.  [Ref. SRD Section 3.3.5 Interchangeability]

# Quality Assurance Provisions

## General

This section identifies the methods to be used for verification of requirements in Section 3.2 of this specification.

## Verification Methods

Verification of qualification shall be by analysis, inspection, or test.  Definition of analysis, inspection, and test is as follows:

Analysis:  Verification of conformance with required characteristics by calculation or simulation, including computer modeling based on established material or component characteristics.

Inspection:  Verification of conformance by measuring, examining, testing, and gauging one or more characteristics of a product or service and comparing the results with specified requirements.

Test:  Verification by physically exercising a component or system under appropriate loads or simulated operating conditions, including measurement and analysis of performance data.

## Quality Conformance

This section establishes the specific methods for verification of requirements in Section 3.

### Verification of Physical Characteristics

#### Verification of Coil Positioning

Upon completion of the MCHP, the relative placement of the Type-A, Type-B, and Type-C coils will be confirmed to be as specified in Section3.2.1.1.  This will be measured using the position of the fiducials on each coil. Final verification shall be performed after all assembly operations, e.g. welding, have been completed. (inspection and analysis)

#### Verification of Electrical Isolation

A meager test shall be performed to verify the requirements as specified in Section 3.2.1.2 The meager test shall be conducted at 150 volts with a leakage current not to exceed than 100 micro amps.

#### Verification of Magnetic Permeability

Magnetic permeability of components (shims, studs, etc.) and welds will be verified by use of a calibrated Severn gauge.

#### Verification of Stud Placement

The required minimum thread length for the stud must be calculated analytically, and measured.  Assurance that the stud threads are not fully engaged will be verified visually.

#### Verification of Stud Pre-Tension

The stud pre-tension will be confirmed by ultrasonic inspection using calibrated equipment (see drawing SE140-190).

#### Verification of Shim Friction

As two adjacent coils are placed together, all shims must be tested by hand to verify that they have good contact with the coils.  Any shims that are loose must be replaced, and then the full set of shims must be tested again.

#### Verification of Shim Length

Interference with winding form or coil wings should be checked, and shims cut as specified in Section 3.2.2.1.3 to avoid any interference.

#### Verification of Shim Welding

The Welds will be visually inspected to verify that weld standards are met as specified in the drawings containing the welding information..

# Comments

If the tensile load is not specified here in this document, there should be a reference to where it may be found.

What does this refer to?

For the studs that have nuts, the threads should be fully engaged.

How does this test relate to the requirement of 3.2.2.1.2?

# Text boxes

Controlled Document

This is a controlled document.  Check the NCSX Engineering Web prior to use to assure that this document is current.

Side - A

Type - C

Type - B

Type - A

Side - A

Side - B

Side - B

Table 1.0   Period Assembly Make-up

Period 1:   MCHP – Left Side            MCHP – Right Side

C1 / B1 / A1                        A2 / B2 / C2

Period 2:   MCHP – Left Side            MCHP – Right Side

C3 / B3 / A3                        A4 / B4 / C4

Period 3:   MCHP – Left Side            MCHP – Right Side

C5/ B5 / A5                        A6 / B6 / C6

Table 1.0   Period Assembly Make-up

Period 1:   MCHP – Left Side            MCHP – Right Side

C1 / B1 / A1                        A2 / B2 / C2

Period 2:   MCHP – Left Side            MCHP – Right Side

C3 / B3 / A3                        A4 / B4 / C4

Period 3:   MCHP – Left Side            MCHP – Right Side

C5/ B5 / A5                        A6 / B6 / C6