NCSX

Structural Analysis Report for Proof Testing

Station 3 Lift Fixture & Lifting Clevis

Document #

Prepared By: ____Mark Smith______________

Prepared By: ____Srinivas Avasarala_________

Reviewed By: ____Tom Brown______________

Reviewed By: ____   Art Brooks______________

Executive Summary

Structural analyses were performed on the Station 3 lift fixture and lifting clevis. The objective was to validate safe proof testing conditions through estimating the anticipated stresses. The lift fixture was analyzed for three proof test configurations. The first configuration, which accounts for the maximum in service load, is from lift point 1, and required a proof load of 22.5 kips. Proof loads of 12.6 kips and 17.1 kips are required for lift points 2 and 3 respectively. Finite element analyses show peak Von Mises stresses of 16.9, 6.63, 6.18 ksi for lift points 1, 2, and 3 respectively. The proof load for the lifting clevis is 36 kips. Analytical results for the clevis show the maximum stresses are located on section 2 and are: max tensile stress 19.7 ksi, max shear stress 4.93 ksi, and max bearing stress of 10.2 ksi. The weld load is 1429 lbf/in.

Table of Contents

List of Figures	iv

List of Tables	iv

List of Equations	iv

Background	1

Lift Fixture Structural Analysis	2

Summary	11

References	12

Appendix	13

# List of Figures

Figure 1. Station 3: Lift Point Layout in Maximum Load Configuration [1].	2

Figure 2.  Lift Point 1: ProMechanica FEM.	3

Figure 3. Lift Point 1: ProMechanica FEA Results.	4

Figure 4. Lift Point 1: Ansys Workbench FEM.	4

Figure 5. Lift Point 1: Ansys Workbench FEA Results.	5

Figure 6. Lift Point 2: Ansys Workbench FEM & Analysis Results.	5

Figure 7. Lift Point 3: Ansys Workbench FEM & Analysis Results.	6

Figure 8. Station 3 Lift Clevis CAD Model.	7

Figure 9. Station 3 Clevis Geometry.	7

Figure 10. Clevis Tension Loading and Section Labels.	8

Figure 11.  Station 3 Lift Clevis FEM.	10

Figure 12. Lift Clevis Maximum Von Mises Stress.	10

Figure 13. ASME Reference Geometry [2].	13

# List of Tables

Table 1. Station 3 Lift Point Proof Loads and Unit Vectors.	3

Table 2. Material Properties.	3

Table 3. Allowable Loads Clevis S1 (a/b).	8

Table 4. Allowable Loads Clevis S2.	8

Table 5. Estimated Clevis Stresses.	9

# List of Equations

Equation 1. Allowable Pin Tensile Strength: [4] eq (3-45).	13

Equation 2. Effective Width Criteria: [4] eq (3-46).	13

Equation 3. Effective Width: [4] eq (3-47).	13

Equation 4. Allowable Single Plane Fracture Strength: [4] eq (3-48).	13

Equation 5. Allowable Double Plane Shear Strength: [4] eq (3-49).	13

Equation 6. Total Area of Shear Planes: [4] eq (3-50 & C3-2).	13

Equation 7.  Allowable Bearing Stress: [4] eq (3-51).	13

# Background

Proof testing is required for all in house fabricated lifting devices/components which include the station 3 lift fixture and lifting clevis. Safety standards require proof testing at 125% of the maximum anticipated in service load. Previous estimated weight for the half period (HP) and lift fixture structure is 24 kips [1]. Furthermore, simulation of station 3 field period assembly revealed maximum in service loads of 18 kips, 10.08 kips, and 13.68 kips, for lift fixture lift points 1, 2, and 3 respectively, refer to figure 1 [1]. Therefore, the required proof testing loads are 22.5 kips, 12.6 kips and 17.1 kips, for lift points 1, 2, and 3 respectively.

The lifting clevis requires proof testing at 30 kips, but, it is used in conjunction with an actuator rated at 32 kips. Therefore, the clevis proof load is 40 kips.

Note: ASME BTH-1-2005 Design of Below the Hook Lifting Devices [2] provides the following comments for evaluation of FEA results used in conjunction with BTH-1-2005.

BTH-1-2005 is based on classical strength of material methods. These methods effectively compute average stresses acting on structural / mechanical elements. The effects of stress concentrations are not normally required for static strength of a lifter, but are most important when determining fatigue life.

Peak stresses due to discontinuities do not affect the ultimate strength of a structural element unless the material is brittle. The types of steel on which this Standard is based are all ductile materials. Thus, static strength may reasonably be computed based on average stresses.

Linear FEA will typically show peak stresses that indicate failure. This is particularly true when evaluating static strength. While the use of such methods is not prohibited, modeling of the device and interpretation of the results demands suitable expertise to assure the requirements of this standard are met without creating unnecessarily conservative limits for static strength and fatigue life.

Therefore, the NCSX structural standards [3] were used as a basis for evaluating FEA results.

Design Tresca Stress Value (Sm):

Sm equals the lesser of : 	(2/3)Yield Strength	 = 24 ksi

(1/2)Ultimate Strength = 29 ksi.

Stress Allowable Primary Stress + Bending Stress Condition: < 1.5Sm = 36 ksi.

Stress Allowable Total Primary Stress + Seconding Stress Condition: < 3Sm = 72 ksi.

Allowable Bearing Stress < Yield Strength = 36 ksi.

Figure 1. Station 3: Lift Point Layout in Maximum Load Configuration [1].

# Lift Fixture Structural Analysis

A finite element model (FEM) of the lift fixture was created and a finite element analysis (FEA) performed using both ProMechanica and Ansys Workbench software platforms. A ProMechanism simulation of the station 3 field period assembly (FPA) facilitated vector estimates of the maximum in service loads [1, 4, 5]. FEA was performed at the loads of 22.5 kips, 12.6 kips and 17.1 kips with corresponding unit vectors for lift points 1, 2, and 3 respectively. Refer to table 1 for lift point proof loads and unit vectors and table 2 for the material properties used in the analysis. Figures 2 and 3 depict the FEA results obtained from ProMechanica, for lift point 1; figures 4 and 5 represent the results from Ansys Workbench. The ProMechanica results show a peak Von Mises stress of 22.8 ksi The Workbench results show a peak Von Mises stress of 16.1 ksi. FEA was performed at lift points 2 and 3 using only the Ansys Workbench platform, figures 6 and 7 display the model and results. FEA for the lift point 2 configuration resulted in a peak Von Mises stress of 6.63 ksi while the lift point 3 configuration resulted in 6.18 ksi. All peak stresses are below the design Tresca stress value Sm, which is significantly below the stress allowable.

Table 1. Station 3 Lift Point Proof Loads and Unit Vectors.

| Lift Points: Proof Loads & Unit Vectors. |  |
| --- | --- |
| Lift Point # | Load Ratio | Magnitude (lbf) | ex | ey | ez |
| 1 | 0.75 | 22500 | -0.15738 | 0.987364 | 0.018506 |
| 2 | 0.42 | 12600 | -0.24121 | 0.967269 | 0.078798 |
| 3 | 0.57 | 17100 | -0.00966 | 0.993034 | 0.11743 |

Table 2. Material Properties.

| Structural Steel A36 |  |
| --- | --- |
| Specific Weight: | γ = 0.284 lbf/in3 |
| Elastic Modulus: | E = 29.0 E3 ksi |
| Rigid Modulus: | G = 11.0 E3 ksi |
| Tension Yield Strength: | Sty = 36 ksi |
| Compression Yield Strength: | Scy = 36 ksi |
| Tension Ultimate Strength: | Stu = 58 ksi |
| Compression Ultimate Strength: | Scu = 58 ksi |

Figure 2.  Lift Point 1: ProMechanica FEM.

Figure 3. Lift Point 1: ProMechanica FEA Results.

Figure 4. Lift Point 1: Ansys Workbench FEM.

Figure 5. Lift Point 1: Ansys Workbench FEA Results.

Figure 6. Lift Point 2: Ansys Workbench FEM & Analysis Results.

Figure 7. Lift Point 3: Ansys Workbench FEM & Analysis Results.

Lift Clevis Analysis

Analytical calculations were performed for the clevis to determine allowable loads and proof test stress levels. Refer to figure 8 for a model of the lift clevis, figure 9 for geometry parameters, and table 2 for the material properties used in the analysis. Additionally, a ProMechanica FEA was performed.

Figure 8. Station 3 Lift Clevis CAD Model.

Figure 9. Station 3 Clevis Geometry.

Analytical Calculations

Figure 10 depicts the loading condition and clevis section labels. Refer to table 3 for the allowable loads on the clevis: section 1 (S1 a/b) and table 4 for the clevis: section 2 (S2). The allowable bearing stress was computed at 15 ksi. Note, the allowable loads/stress are based on equations from ASME Design of Below the Hook Lifting Devices [2], refer to appendix A for the relevant equations. Table 5 lists the estimates for the clevis stresses at the proof load of 40 kips; results based on equations from [6]. Note, maximum bearing stress during proof test is estimated at 10.2 ksi, 67.7% of the allowable. Based on equations [7], the weld load is 1429 lbf/in. Using  1/4 fillet weld (2800 lbf/in of weld) provides a weld safety factor of about 1.5.

Figure 10. Clevis Tension Loading and Section Labels.

Table 3. Allowable Loads Clevis S1 (a/b).

| Pt1 | 78880 | lbf | Allowable Tensile Strength through Pin Hole |  |
| --- | --- | --- | --- | --- |
| Pb1 | 56768 | lbf | Allowable Single Plane Fracture Strength beyond Pin Hole |
| Av1 | 5 | in^2 | Total Area of Shear Planes beyond Hole. *NOTE: curved edges |
| Pv1 | 52420 | lbf | Allowable Double Plane Shear Strength beyond Pin Hole. |

Table 4. Allowable Loads Clevis S2.

| Pt2 | 117813 | lbf | Allowable Tensile Strength through Pin Hole. |  |
| --- | --- | --- | --- | --- |
| Pb2 | 94665 | lbf | Allowable Single Plane Fracture Strength beyond Pin Hole |
| Av2 | 8 | in^2 | Total Area of Shear Planes beyond Hole. *NOTE: curved edges |
| Pv2 | 91528 | lbf | Allowable Double Plane Shear Strength beyond Pin Hole. |

Table 5. Estimated Clevis Stresses.

| Estimated Tensile Stress |  | Estimated Shear Stress |
| --- | --- | --- |
| S1a or S1b |  |  |  | * Double Plane Shear Area |  |
| Gross Area | 8 | in^2 |  | S1a & S1b |  |  |
| Tensile Stress | 2500 | psi |  | Total Shear Area | 4.65 | in^2 |
| Net Area | 4.90 | in^2 |  | Shear Stress | 4303 | psi |
| Tensile Stress Net | 4085 | psi |  | S2 |  |  |
| S2 |  |  |  | Shear Area | 8.12 | in^2 |
| Gross Area | 11.25 | in^2 |  | Shear Stress | 4929 | psi |
| Tensile Stress | 3555.556 | psi |  |  |  |  |
| Net Area | 7.31 | in^2 |  |  |  |  |
| Tensile Stress Net | 5470 | psi |  |  |  |  |
|  |  |  |  | Estimated Bearing Stress |
| Accounting for Stress Concentrations |  | S1a & S1b |  |  |
| Reference [1] , page 985 Fig A-15-12 |  | Project Area | 2.94 | in^2 |
| Hole Stress Riser |  |  |  | Bearing Stress | 6807 | psi |
| S1a or S1b |  |  |  | S2 |  |  |
| h1/w1 | 0.4 |  |  | Projected Area | 3.94 | in^2 |
| d1/w1 | 0.4 |  |  | Bearing Stress | 10159 | psi |
| K1 | 3.5 |  |  |  |  |  |
| Max Tensile Stress | 14297 | psi |  |  |  |  |
| Hole Stress Riser |  |  |  |  |  |  |
| S2 |  |  |  |  |  |  |
| h2/w2 | 0.5 |  |  |  |  |  |
| d2/w2 | 0.35 |  |  |  |  |  |
| K2 | 3.6 |  |  |  |  |  |
| Max Tensile Stress | 19692 | psi |  |  |  |  |
| Reference [1] , page 985 Fig A-15-5 |  |  |  |  |
| Fillet Stress Riser |  |  |  |  |  |  |
| S2 |  |  |  |  |  |  |
| D/d | 1.11 |  |  |  |  |  |
| r/d | 0.44 |  |  |  |  |  |
| K3 | 1.35 |  |  |  |  |  |
| Max Tensile Stress | 4800 | psi |  |  |  |  |

Lift Clevis FEA

Refer to figure 11 for the ProMechanica FEM and figure 12 for the FEA stress results. The FEM consisted of the 3 pins contact interfaced with the clevis. Also, weak springs were added to eliminate open degrees of freedom. A peak Von Mises stress of 42.1 kips was found on the clevis section 2, refer to figure 12.

Figure 11.  Station 3 Lift Clevis FEM.

Figure 12. Lift Clevis Maximum Von Mises Stress.

# Summary

# References

1. Brown, T. Analysis performed on the FPA station 3 lift fixture for its FDR

NCSX-CALC-18-002-00. 10 Dec. 2007.

2. ASME. BTH-1-2205 Design of Below the Hook Lifting Devices. 2006.

3. Zatz, I. J., NCSX Structural Design Criteria NCSX-CRIT-CRYO-00. 2004.

4. Brown, T. Excel File: trace00_path5tom3r13right.xls.

5. ProMechanism Simulation Files: stb-fpa_mech_leftside.asm, stb-fpa_mech_rightside.asm.

6. Shigley. Machine Design 7th ed. 2004.

7. Blodgett, O, W. Design of Welded Structures. 1966.

# Appendix

Refer to figure 14 for applying equations 1-6.

Equation 1. Allowable Pin Tensile Strength: [2] eq (3-45).

Equation 2. Effective Width Criteria: [2] eq (3-46).

Equation 3. Effective Width: [2] eq (3-47).

Equation 4. Allowable Single Plane Fracture Strength: [2] eq (3-48).

Equation 5. Allowable Double Plane Shear Strength: [2] eq (3-49).

Equation 6. Total Area of Shear Planes: [2] eq (3-50 & C3-2).

Figure 13. ASME Reference Geometry [2].

Equation 7.  Allowable Bearing Stress: [2] eq (3-51).

# Comments

I thought there is a ½ in fillet weld?