PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # _____

# COGNIZANT INDIVIDUAL:  Tom Brown

# ECN TITLE:	Field Period Assembly Fixture Modifications

# CC/WP/Job:  9450/1***/1803		AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:  _______

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE185-304 | 0 | MCWF HP Assy w/Sissco Lifting System for Positioning over VV |
| SE185-314 | 0 | MCWF HP Lifting Fixture Frame Assemblies |
| SE186-325 | 0 | MCWF Support Cart Support Post Weldment |
| SE186-331 | 0 | MCWF Support Cart Miscellaneous Details |
| SE186-333 | 0 | Adjuster Bar Support Structure Weldment |
| Continued on back. |

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments)

SE185-304 – Revised hardware material ; replaced SC185-325 with SC185-326

SE185-314 – Revised hardware material

SE186-325 – Added 3” locating dimension

SE186-331 – Revised # of c’bore holes from 18 to 23 places

SE186-333 – Revised Pusher Support Channel callout in B/M – 6” x 13# channel was 25#

# REASON FOR CHANGE:

SE185-304 – Grade 8 hardware (nut, flat washer, lock washer) not req’d; SC185-326 added for new lift configuration.

SE185-314 – Hardware callout to reflect Grade 8 requirements

SE186-325 – Dimension was missing for part location on post

SE186-331 – Revised to reflect proper number of holes in part

SE186-333 – Incorrect channel size specified

ENGINEERING CHANGE NOTICE APPROVALS	:		DATE:

# COGNIZANT INDIVIDUAL MAKING CHANGE:

# RESPONSIBLE LINE MANAGER:

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN # _____

# COGNIZANT INDIVIDUAL:

# ECN TITLE:

# CC/WP/Job:	AREA OR PROJECT:

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |