NCSX

Station 5 Structural Analysis

Hoist & Base Support

Document #

March 6, 2008

Prepared By: ____Mark Smith______________

Prepared By: ____________________________

Prepared By: ____________________________

Reviewed By: ____________________________

Executive Summary

Table of Contents

List of Figures	iv

List of Tables	iv

List of Equations	iv

Introduction	1

Purpose	1

Scope	1

Methodology	2

Hoist Structural Integrity	2

Hoist Structure & Cabling Pin Connection	2

Hoist-Modular Coil Bolted Connection	6

Station 5 Structural Support Integrity	8

Buckling Analysis	8

Results & Discussion	13

Conclusion	14

References	15

Appendix	16

# List of Figures

Figure 1. FEA #1 Results Convergence and Deformation.	2

Figure 2. FEA #1 Results Pin Connection .	3

Figure 3. FEA #2 Results Von Mises Stress.	4

Figure 4. FEA #2 Results Displacements.	5

Figure 5. (a) FEM Loads & Constraints, (b) FEM Mesh.	9

Figure 6. Buckling Analysis (a) Mesh Parameters, (b) Mesh Image.	11

Figure 7. Torque-Preload Curve Typical Nut Factor: K=0.15.	19

Figure 8.  Torque-Preload Curve Typical Nut Factor: K =0.20.	19

# List of Tables

Table 1. Reactions from FP Model 30608.	10

Table 2. Bolt Specifications and Preload	17

Table 3. Bolt Thread Specifications [4]	18

Table 4. Maximum Torque Specifications for Preload	18

# List of Equations

Equation 1. Critical Buckling Load.	10

Equation 2. Critcial Buckling Stress.	10

# Introduction

## Purpose

The purpose of this study was to investigate the structural integrity of the station 5 field period assembly hoist (FPAH), the hoist to machine bolted connections, and the station 5 support base. The objective was to ensure the devices will operate within allowable limits.

## Scope

The analysis of the hoist encompassed the following:

- Validation of the hoist design structural integrity.

- Determination of required bolt preloads and corresponding torque.

- Validation of bolted connection integrity for the hoist-machine interface.

The analysis of the support base consisted of the following:

- Buckling Analysis

- Determination of Bearing Stress.

- Support Base Reactions Under Impact Loading.

# Methodology

## Hoist Structural Integrity

### Hoist Structure & Cabling Pin Connection

Results from FEA

Analytical Results

Lug Calculations

A finite element model (FEM) was created from ProEngineer (ProE) files and used for analysis in the Mechanica platform of the ProE environment.

FEA #1 ms_22708_v1_sta5_hoist_fea2 : Main Structural Beam Initial Design

FEM consisted of channels and webs bonded via contacting surface area.

No Secondary Beam or cross plates included in this model.

Mesh settings all default except detailed fillet modeling enabled.

Analysis settings: Multi-pass Adaptive, polynomial degree 9, convergence 5% on local displacement, strain energy, global stress.

Figure 1. FEA #1 Results Convergence and Deformation.

Figure 2. FEA #1 Results Pin Connection .

FEA #2 ms_22708_v1_sta5_hoist_fea1 : Entire Hoist.

CAD model: ms-22708_v1_sta5_hoist_fea.asm

FEA: ms_fea2_3708_entire_hoist.rwd

FEM consisted of channels and webs bonded via contacting surface area.

Attempted to simulate welds on secondary Beam using a Mate offset of 0.0050 inch.

But, the offset did not stop the surface bonding. Thus, the bond was achieved through both the fillets and surface contact area.

Cross plates offset 0.020 inch, bond achieved through fillet to simulate welds.

Mesh settings all default except detailed fillet modeling enabled.

Analysis settings: Multi-pass Adaptive, polynomial degree 6, convergence 10% on local displacement, strain energy, global stress.

Refer to figures 3 & 4 for the analysis results.

Figure 3. FEA #2 Results Von Mises Stress.

Figure 4. FEA #2 Results Displacements.

Analytical Calculation for Lug Loading

Figure 5.  Hoist Lug Analytical Model.

Table 1. Hoist Luh Analytical Results.

| CAD Model Parameters |  |  |  |  |
| --- | --- | --- | --- | --- |
| a | 2.4375 |  |  |  |  |  |
| Dp |  |  |  |  |  |  |
| be | 1.6875 |  |  |  |  |  |
| Dh | 2.125 |  |  |  |  |  |
| R | 3.5 |  |  |  |  |  |
| r |  |  |  |  |  |  |
| t | 2 |  |  |  |  |  |
| Material Properties |  |  |  |  |
| Fy | 3.60E+04 | psi | ref [3] |  |  |  |
| Fu | 5.80E+04 | psi | ref [3] |  |  |  |
| Design Factors |  |  |  |  |  |
| Nd | 2.4 |  | ref [3], [8] |  |  |
| Computations |  | Check Value < be | Reference [8] |
| beff | eq1 | eq2 | eq1 | eq2 | min |  |
|  | 8 | 1.8305 | 1.6875 | 1.6875 | 1.6875 |  |
| Pt | 135937.5 | lbf | Allowable Tensile Strength of Pin |
| Pb | 145793.6 | lbf | Allowable Single Plane Fracture Strength of Pin |
| Av | 10.9948 | in^2 | Total Area of Shear Planes beyond Hole |
| Pv | 154996.1 | lbf | Allowable Double Plane Shear Strength beyond Pin Hole. |

### Hoist-Modular Coil Bolted Connection

Bolt Preload: Refer to the Appendix tables 3,4, 5 and figure 7 & 8.

Joint Separation Analysis

Equation 1.  Load to Separate Joint.

Equation 2. (a-c) Bolt stiffness.

Equation 3.  Joint Member Stiffness.

Equation 4. Joint Total Stiffness.

Figure 6. Member Stiffness Frustum Cone Model [1].

Table 2. Joint Separation Analysis.

| Joint Member Parameters |  |  | degree | radian |
| --- | --- | --- | --- | --- |
|  |  |  |  |  | alpha: ά | 30 | 0.523599 |
| Bolt Shaft Nominal Diameter |  | 1.00 | in | Member | Stiffness | Units |
| Bolt (B1) Head Diameter |  | 1.69 | in | B1: kb | 4.82E+06 | psi |
| Elastic Modulus: B1 |  | 3.00E+07 | psi | FW1: k1 | 3.20E+08 | psi |
| B1 | At |  | 0.606 | in^2 | HMB: k2 | 7.58E+07 | psi |
| B1 | Ad |  | 0.770546 | in^2 | LW: k3 | 2.31E+08 | psi |
| Length of Bolt |  |  | 4.5 |  | FW2: k4 | 6.18E+08 | psi |
| Length of Threads |  | 2.25 | in | MCS: k5 | 9.51E+07 | psi |
| Grip Length |  |  | 4.25 |  |  |  |  |
| Threads not in Grip |  | 0.25 |  | D1 | 1.69 | inch |
|  | lt |  | 2.00 |  | D2 | 1.877252086 | inch |
|  | ld |  | 2.25 |  | D3 | 1.84 | inch |
| Flat Washer #1 (FW1) Thickness |  | 0.16 | in | D4 | 2.189338365 | inch |
| Elastic Modulus: FW1 |  | 3.00E+07 | psi | D5 | 2.374090451 | inch |
| Hoist Mount Block (HMB) Thickness | 2.13 | in |  |  |  |
| Elastic Modulus: HMB |  | 3.00E+07 | psi | Joint Stiffness per Bolt |  |
| Nut Height |  |  | 0.984375 | in | km | 3.05E+07 | psi |
| Nut Head Diameter |  | 1.84 | in |  |  |  |
| Lock Washer (LW) Thickness |  | 0.31 | in |  |  |  |
| Elastic Modulus: LW |  | 3.00E+07 | psi | Load per Bolt to Separate Joint with |
| Flat Washer #2 (FW2) Thickness |  | 0.16 | in | PreLoad = | 47691 | lbf |
| Modular Coil Section (MCS) Thickness | 1.50 | in |  |  |  |
| Elastic Modulus: MCS |  | 2.10E+07 | psi | P0 | 55226.87 | lbf |

FEA of Hoist Modular Coil Connection

FEA figures have STRESS in ProE Mechanica default units unless otherwise specifically stated.

CAD model filename: sta5-HOIST-MT-Blk-22008-FEA1.asm.1

Mechanica Results filename: ms_fea1_30708-hoist_modcoil.stt

NOTE: FEA may be compromised. Displacement model had merged parts, need to investigate or call for support to resolve concern.

Modular coil mounting section re-modeled for FEA, refer to figure XX for the FEM.

Connection modeled with ProE “built in” bolted connection, refer to figure XX, for the bolt model parameters.

NOTE: FEA may be compromised. Displacement model had merged parts, need to investigate or call for support to resolve concern.

Bearing Stress

Table 3. Bearing Stress Hoist Modular Coil connection.

| Bolt | Bolt |  |  |
| --- | --- | --- | --- |
| PreLoad (lbf) | FEA Loading (lbf) |  |  |
| 51791 |  | Bearing Stress (lbf/in^2) |
|  | Area (in^2) | PreLoad | Total Load |
| Bolt Head | 1.119039185 |  |  |
| Flat Washer Series R | 3.944729035 | 46281.668 | 0 |
| Under Flat Washer |  | 13129.1654 |  |
| Nut | 1.416451837 |  |  |
| Lock Washer | 1.446251028 | 36563.8977 |  |
| Under Lock Washer |  |  |  |

Balance Cabling Connections

1. TF Coil Holes

2. Mounting Bracket

## Station 5 Structural Support Integrity

### Buckling Analysis

Part 1: Static analysis used to obtain reactions loads, refer to table 1.

ProE Mechanica results filename: ms_4jacks_fea_a1_30608.stt

See figure 2(a-b) for mesh parameters.

7.77 & 7.78 distances to center.

Analysis performed 3/8/06. The associated files are as follows:

PRoE Standard Application filename: SMS-STATION5-MODEL-FEA.ASM.1

ProE Mechanica Application results filename: ms_FP_model_fea_3608_v2

Datum points were inserted at approximately the center of the contacting surface of the jack stand at the FP/jack stand interface. These points were constrained in all 6 degree of freedom (DOF). The field period weight was positioned at the estimated center of gravity and used for the analysis loading conditions The finite element mesh was created from nodes manually and automatically generated. Refer to figure 1(a & b) for the model set up.

Figure 7. (a) FEM Loads & Constraints, (b) FEM Mesh.

Table 4. Reactions from FP Model 30608.

| Location | Reaction Fx | Reaction Fy | Reaction Fz | Moment x-axis | Moment y-axis | Moment z-axis |
| --- | --- | --- | --- | --- | --- | --- |
| Jack 1 (28.21, 43.62, 24.49) | 4.060E3 lbf | 20.40E3 lbf | 3.789E3 lbf | 0 | 0 | 0 |
| Jack 2 (28.21, 43.41, -24.49) | 3.121E3 lbf | 20.155E3 lbf | -4.049E3 lbf | 0 | 0 | 0 |
| Jack 3 (-10.28, 37.87, -15.6) | -2.532E3 lbf | 19.987E3 lbf | -1.453E3 lbf | 0 | 0 | 0 |
| Jack 4 (-10.28, 37.87, 15.6) | -4.649E3 lbf | 19.570E3 lbf | 1.713E3 lbf | 0 | 0 | 0 |

Buckling Analytical Analysis

Analysis using Euler Equation for Elastic Buckling [7].

Assumptions:

1. Load acts through centroid of the cross section area of the beam.

2. Beam is perfectly straight when initially loaded.

3. Beam composition is homogenous.

4. Deflections are small and within the elastic limit.

5. Beam is supported free at the applied load end and fixed at the other end.

Equation 5. Critical Buckling Load.

Equation 6. Critcial Buckling Stress.

Figure 8. Jack Stand Support Beam.

where E is The elastic modulus of the material, I is the area moment of inertia, K is the effective-length factor, L is the length of the beam, and A is the area of the cross section. Refer to figure for an image of the beam section. Refer tp table XX for the beam parameters and the calculation results.

Table 5. Buckling Analysis.

| Parameters |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| Beam W8x31 |  |  |  |  |  |
| Cross Sectional Area | A | 9.13 | in^2 |  |  |
| Area Inertial Moment | Ix | 110 | in^4 |  |  |
| Radius of Gryration | rx | 3.47 | in |  |  |
| Area Inertial Moment | Iy | 37.1 | in^4 |  |  |
| Radius of Gryration | ry | 2.02 | in |  |  |
| Effective-Length Factor | K | 0.5 |  |  |  |
| Elastic Modulus | E | 3.00E+07 | psi |  |  |
| Length of Beam | L | 21 | in |  |  |
|  |  | Axis 1 (x) | units | Axis 2 (y) | units |
| Critical Load | P | 2.95E+08 | lbf | 9.96E+07 | lbf |
| Critical Stress | σ | 3.24E+07 | psi | 1.09E+07 | psi |

CAD model filename:sms-station-model-fea.asm

Mechanica FEA filename: ms_4jacks_fea_a1-30608.rwd

Units are in psi.

Impact Analysis

# Results & Discussion

# Conclusion

# References

1. Machine Design 7th ed. Shigley 2004.

2. Multiple Coil Lift Calculation. PPT file. HM Fan.

3. Analysis performed on the FPA station 3 lift fixture for its FDR. NCSX-CALC-18-002-00.

Brown. 10 Dec. 2007.

4. Machinery's Handbook. 26th ed. Threads and Threading

5. Handbook for Bolted Joint Design. NCSX-CRIT-BOLT-00. HM Fan. 2007.

6. NASA Reference Publication 1228. Fastener Design Manual. 1990

# Appendix

Table 6. Bolt Specifications and Preload

| SAE J429 1-8 UNC Bolt |  |  |  |
| --- | --- | --- | --- |
|  | Value | Units | Notes |
| Proof Strength | 1.2000E+05 | psi |  |
| Yield Strength | 1.3000E+05 | psi |  |
| Tensile Strength | 1.5000E+05 | psi |  |
| Tensile Strength of Nut | 1.5000E+05 | psi |  |
| Number of Threads per Inch: n | 8 | quantity | reference [1] |
| Pitch: P | 0.125 | in | derived |
| Minor Diameter Area: A1 | 0.551 | in^2 | reference [1,4] |
| Maximum Minor Diameter: d1[4] | 0.849 | in | reference [4] |
| Minimum Diameter: d1 | 0.838 | in | derived |
| Basic Major Diameter: d | 1.000 | in | reference [1] |
| Mean Diameter: Davg | 0.919 | in | derived |
| Height of Threads: H | 0.108 | in | derived, equation [1] |
| Minimum Pitch Diameter: d2[2] | 0.910 | inch | reference [2,4] |
| Minimum Pitch Diameter Computed: d2 | 0.919 | in | derived, equation [1] |
| Basic Pitch Diameter: Pb | 0.919 | in | reference [4] |
| Tensile Stress Area Computed: At | 0.606 | in^2 | derived |
| Tensile Stress Area: At | 0.606 | in^2 | reference [1,4] |
| Tensile Stress Area: At[2] | 0.594 | in^2 | reference [2] |
| Shear Area of Bolt: As[2] | 1.187 | in^2 | reference [2] |
| Shear Area of Internal Thread (nut): An[2] | 1.673 | in^2 | reference [2] |
| Minimum Engagement Length: Le[2] | 0.717 | in | reference [2] |
| Maximum Minor Diameter Internal Thread: Kn | 0.890 | in | reference [4] |
| Maximum Pitch Diameter Internal Thread: En | 0.928 | in | reference [4] |
| Minimum Engagement Length: Le | 0.684 |  | derived |
| Engagement Length per Nut Thickness: Ln | 0.956 | in | reference [4] |
| Shear Area of Bolt: As | 1.211 |  | derived |
| Shear Area of Internal Thread (nut): An | 1.598 |  | derived |
| Force to Break Bolt: Fbb | 90862.141 | lbs | derived |
| Force to Shear Bolt Threads: Fsb | 90862.141 | lbs | derived |
| Force to Shear Nut Threads: Fsn | 119825.625 | lbs | derived |
| Preload: P0[2] | 49200.000 | lbs | reference [2] |
| Relaxation 5%---Effective Preload: Pe[2] | 46740.000 | lbs | reference [2] |
| Preload per Ref [2] equation: P0 | 50201.333 | lbs | derived, equation [2] |
| Relaxation 5%---Effective Preload: Pe | 47691.266 | lbs | derived |
| Preload per Ref [5] equation: P0' | 54517.285 | lbs | derived, equation [5] |
| Relaxation 5%---Effective Preload: Pe' | 51791.420 | lbs | derived |

Table 7. Bolt Thread Specifications [4]

| External Threads |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | Major Diameter | Pitch Diameter |  |
| Class | max | min | max | min |  |
| 2A | 0.9980 | 0.983 | 0.9168 | 0.91 |  |
| Internal Threads |  |  |  |  |
|  | Minor Diameter | Pitch diameter | Major Diameter |
| Class | min | max | min | max |  |
| 2B | 0.865 | 0.89 | 0.9188 | 0.9276 | 1 |

Table 8. Maximum Torque Specifications for Preload

|  | Torque Required to Achieve Preload at | P0= |  | 50201.33 | lbs. |
| --- | --- | --- | --- | --- | --- |
|  | with Relxation of 5% Effective Preload: | Pe= |  | 47691.27 | lbs. |
|  |  | Torque: inch-lbs. | Torque: ft-lbs. |
| Torque Wrench Method | K=.2 | K=.15 | K=.2 | K=.15 |
|  | Un-Lubricated Bolts: Torque Error ± 35% | 7437.23 | 5577.93 | 619.77 | 464.83 |
|  | Lubricated Bolts: Torque Error ± 25% | 8032.21 | 6024.16 | 669.35 | 502.01 |
| Hydraulic Tensioner: |  |  |  |  |
|  | Torque Error ± 15% | 8730.67 | 6548.00 | 727.56 | 545.67 |
|  | Torque Required to Achieve Preload at | P0= |  | 54517.28 | lbs. |
|  | with Relxation of 5% Effective Preload: | Pe= |  | 51791.42 | lbs. |
|  |  | Torque: inch-lbs. | Torque: ft-lbs. |
| Torque Wrench Method | K=.2 | K=.15 | K=.2 | K=.15 |
|  | Un-Lubricated Bolts: Torque Error ± 35% | 8076.63 | 6057.48 | 673.05 | 504.79 |
|  | Lubricated Bolts: Torque Error ± 25% | 8722.77 | 6542.07 | 726.90 | 545.17 |
| Hydraulic Tensioner: |  |  |  |  |
|  | Torque Error ± 15% | 9481.27 | 7110.95 | 790.11 | 592.58 |
| NOTE: K is typical nut factor: |  |  |  |  |
| Recommended K = 0.2 for un-lubricated and K = 0.11 to 0.15 lubricated: reference [5] |
| Recommended K = 0.15 for steel on steel: reference [6] |  |  |

Figure 9. Torque-Preload Curve Typical Nut Factor: K=0.15.

Figure 10.  Torque-Preload Curve Typical Nut Factor: K =0.20.

# Text boxes

t2

D3

D2

d

ά

t1

D1