TO:   		Bob Ellis

FROM:  	Mark Smith

SUBJECT:	Shim Thickness Predictions

Date:	10/23/08

NOTE: Unless otherwise stated, all relevant files can be found at: P:\public\anonymous ftp private\bob-simmons+sig03\Smith\BU Files for Shim Thickness Calculations\Shim GUI\Shim Thickness GUI Files

Background

Precise positioning of the modular coils (MC) was required for the NCSX. This was to be accomplished through stringent dimensional control and the extensive use of metrology. After the MC’s were fabricated, distortional adjustment and metrology procedures were performed to characterize the as-built condition. Specifically, metrology surface scans were performed on the coil flanges. This data was use to predict the initial shim thicknesses. Refer to figure 1 for an image of the A, B, and C coils with shim and flange labels.

Scope

The scope of this work encompassed all modular coils and consisted of predicting the initial shim thicknesses required for field period assembly. Additionally if it was decided to compensate for as-built errors (i.e. coil re-alignment) data transformation was applied and then the shim thicknesses predicted.

Status

Initial shim thicknesses were predicted for only the MC’s used to build the 1st field period. All remaining MC interfaces require initial shim thickness predictions. See Folder: Shim Thickness Calculations\Shim GUI\Shim Thickness GUI Files.

Method

Matlab was used to create a graphical user interface (GUI) which facilitated the computations. To run the GUI open the file: gui_61908_r1_shim_thickness.fig. Overall, using the GUI consisted of selecting the desired MC joint; reading into Matlab various data files: shim corner locations, flange surface scan data, re-alignment matrices; calculating thicknesses; and plotting various information. Refer to figure 2, 3, and 4 for an image of the GUI, the Help Display and plotted data examples. The flange scan data can be found at the respective close out location. The shim corner locations and re-alignment matrix files could be found at the location cited above.

Note 1: The Help Menu provides a step by step guide to use the GUI.

Note 2: The various files associated with the GUI contain detailed descriptions and explanations.

Lessons Learned

The metrology data used should be “cleaned”. This means it was evaluated/visually inspected to ensure that erroneous points were removed. This should have occurred prior to the data being achieved. However, it’s best to verify it. Verification can be performed by plotting the raw data via the GUI. Using standard Matlab menu options for figures, the plotted data can be rotated and zoomed to inspect for points of concern. If erroneous points are found, they require manual removal.

Figure 1. Coils, Flanges, Shims.

Image modified from:  Stellarator Core Design Overview.pdf  B. Nelson. May 2004.  NCSX Final Design Review for Vacuum Vessel Subassembly and Modular Coil Winding Forms.

Figure 2. Shim Thickness GUI.

Figure 3. Help Display.

Figure 4. Example Plots

# Text boxes

Plot of Predicted Thickness at the Respective Locations in 3D space.

Histogram Plot of Predicted Thickness Values

3D Plot of Surface Scan Data.