# PART I - DESCRIPTION

| WBS Number: 52 | Title: NCSX Central Facilities I&C |
| --- | --- |
| Originator: G. E. Oliaro |
| Description General Description of Work to be Performed: The central process control system will provide supervisory control and a common user interface to all engineering subsystems and high-energy systems. It will provide the synchronization between two or more operating machines at PPPL using shared power conversion resources. It will support current and historical trending, alarm logging, mimic displays, machine state archival, and process control and monitoring functions for NCSX. It will be designed using the Experimental Physics and Industrial Control System (EPICS). The following subsystems will be supported with control and display pages: WBS 2. Thermocouples NBI, Water, Coil, VV WBS 2.1 Fueling Systems WBS 2.2 Vacuum Pumping Systems WBS 2.3 First Wall Conditioning, Bakeout, GDC WBS 2.4 RF Heating Systems HHFW, ECH WBS 2.5 Neutral Beam Heating Systems WBS 4.2 Motor Generators WBS 4.3 Magnet Power Systems WBS 6.2 Water Systems WBS 6.3 Cryogenic Systems Description of Existing Equipment/Facilities to be Reused: No existing equipment from previous machines will be used in this activity. Description of Major Modifications Required to Existing Equipment/Facilities: No major modifications to existing equipment or facilities will be required. |