SUMMARY DESCRIPTION

The NSCX Central Safety Interlock System (CSIS) for CD-4 shall be in conformance with all PPPL Safety standards per ES&H 5008.  The manner of implementation for CD-4 milestone will be optimized to minimize initial cost.  The system will be substantially upgraded after CD-4 to provide a system with attributes that favor minimal life-cycle costs and integrated operations.

LEVEL OF PROTECTION FOR PERSONNEL SAFETY WILL BE SAME AS THAT FOR TFTR OR NSTX.  KIRK-KEY LOCKS WILL BE PROVIDED AS NEEDED. ALL THESE WILL BE ENHANCED WITH ADMINISTRATIVE CONTROLS.

Key Components:

- Hardwired and relay logic with home-run cabling

- Appropriate electrical isolation for ‘unsafe’ areas

- Distributed Global E-Stop Buttons

- Redundant Test Cell Door-Monitoring Switches

- Interlocked Card Reader Access to NCSX Test Cell

- Interface with High-Energy SubSystems (C-Site Rectifiers) per TFTR/NSTX methodology:

  - No E-Stop Command

  - Enable Permissive

  - Arming Permissive

  - Disabled Annunciation

  - Disarmed Annunciation

- COE Control Station near NCSX door:

  - Indicator Lights

  - Kirk Key (electrical) switches