# PART I - DESCRIPTION

| WBS Number: 56 | Title: NCSX Central Safety Interlock System |
| --- | --- |
| Originator: G. E. Oliaro |
| Description General Description of Work to be Performed: The Central Safety Interlock System will provide system wide coordination of personnel and hardware interlocks. Its primary man machine interface will be EPICS. The Central Safety Interlock System will be a fail-safe, hybrid system. Mechanical components and hardwired devices will provide primary protective functions. Redundant PLC technology with redundant sensors will be used to achieve effective, safety system capabilities. Each NCSX high-energy subsystem will interface with the Central Safety Interlock System. A badge reader access control system will restrict access to the Test Cell for only authorized/trained personnel. UPS and Standby power will power critical components. Description of Existing Equipment/Facilities to be Reused: NCSX high energy subsystems will provide their own existing D-site and C-site safety interlocks. It will be assumed that all existing subsystem safety interlocks will have built in redundancy and self-protection. Description of Major Modifications Required to Existing Equipment/Facilities: No major modifications to existing D-Site subsystem safety interlocks will be required. |