Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

Assembly Steps/Major Activities

Potential Issues

Mitigation Plans

# Text boxes

- Component Preparations

- Cut-off short dome port & install insulation system & heater tape/thermocouples system around all ports

- Pre-Installation Set-Up

- Install period support fixture.

- Install FPA on support stand & engage base of MC.

- Install internal & external working platforms

- VV Port Installation

- Install domes, inserting the long port through the MC hole opening & weld dome shell to VV.

- Install small dome ports & remaining circular ports. Leak check after each port is welded.

- Port Boot Seal Assembly Installation

- Install boots on all ports (except Port 4)

- Floor not stiff enough

- Support fixture not stiff enough for personnel access

- Reinforce can be added to substructure

- Consider photogrametry

- Reinforce support fixture with I-beams, etc

Final measurements not within tolerances

Boots do not fit.

- Trim coil assembly concepts not supported by detailed drawings

- Existing hardware on MC interferes with trim coil supports

Custom fit boots as needed

6.0 Install MC Lead/Coolant Connections

- Install MC coolant  lines on each MC & position for TF coil installation & routing through PF structure

- Move working platforms as necessary for TF coil installation

- Install Right TF Coil Assemblies

- Install Left TF Coil Assemblies\

Note: 6.0 & 7.0 have identical processes

- Rotate 2 individual TF coils over MC & temporarily support from B & C coils. (Note: final TF coil for this side and left side of FPA cannot be installed until Station 6)

- Attach temporary supports as needed, disengage base of MC, & install TF support brackets

- Slide TF assemblies against TF support brackets one at a time

- Install machine support plates & re-engage base of MC

- TF Fit-Up Checks

- Perform a fit-up check of the 4 TF coils

- Tack Port 4’s

- Tack weld Port 4’s & install boots

Concepts not fully supported by detail drawings of routings

Design still evolving – schedule supports time to develop detailed plans and procedures.

- Concepts not fully supported by detailed drawings

- Interferences preclude installation of TF coil assemblies

- Damage components during assembly (highly unlikely)

- Buffer and protect individual components

- Install physical stops to prevent motion

Unlikely since checked at vendor – if necessary, remove & replace with acceptable coil and repair

Fit-up of wedges unacceptable due to out-of-tolerance conditions

- Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures.

- Interferences – reassess options to resolve interferences => may require some disassembly (highly unlikely due to large clearances)

- Damage to component – remove TF coil assemblies from Period & repair damaged component on MC or replace

- Install Right TF  Assemblies

Major Activities

- Transfer completed period to Station 6

REPEAT FOR PERIODS 2 & 3

Transfer lift fixture too flexible and allows components to clash during transport

NONE IDENTIFIED??

Diagnostic lead routing concepts not fully supported by detail drawings of routings

- Tolerances a problem at W-7X – revisit NCSX tolerances (NCSX VV ports have 1” radial tolerance/port holes have ½” TPT)

- Difficulty of welders working inside VV in contorted positions may pose ergonomic & confined space hazards

- Support structure may interfere with  lower ports installation

- Leak check fails on one or more ports

- Install PF Structural Members & rout MC leads and coolant lines

- Install PF support structure around TF coils and rout MC leads and coolant lines

- Install MC Coolant Manifold

- Install MC coolant manifold outside the PF coils (in area of PF-6) & connect all MC coolant lines (40 top and bottom each)

- Install Rogowski Coils

- Install Rogowski coils on each end of VV (left side) & route leads initially between space by Port 8 & spool piece opening

- Final Measurements

- Obtain set of Period 1 alignment fiducials for lacatin VV within the MC

- Using laser, align tooling balls on each MCHP

- Using monuments on VV  for alignment, perform trial VV   alignment, adjusting VV supports as necessary.

- Install/verify three preliminary primary fiducials to be used in positioning the period in Station 6.

- Make final measurement of all fiducials, VV end flanges, & Type C end flanges

- Perform final checks and acceptance tests.

- Tolerances - install port within radial clearance with port hole as-built – may require physics evaluation to understand impact on diagnostics.

- Egonomic/confinced space hazards – prior will consider all hazards, however, schedule contingency may be required

- Support structure interferences -  review support structure/lower port clearance in advance &  provide installation tooling as needed

- Identify leak point(s), repair weld and re-test

\

- Trim Coil Installation

- Install trim coil supports onto MC

NEED TOM BROWN INPUT HERE!

- Trim coil assembly concepts - design still evolving – schedule supports time to develop detailed plans and procedures

- MC interferences - designing trim coil supports earlier in schedule to provide location template to review positioning in advance.

MC leads and coolant line routing concepts not fully supported by detail drawings of routings

NONE IDENTIFIED

MC leads and coolant line routing concepts not fully supported by detail drawings of routings

Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures.

Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures

Concepts not fully supported - design still evolving – schedule supports time to develop detailed plans and procedures

- Review design for potential minor adjustments to accommodate out-of-tolerance issues.

- Back Office determine impact of out-of-tolerances o performance

- Project assess steps necessary to recover tolerances if unable to accept out-of-tolerance conditions