| LIFT TITLE: Lifting the Modular Coil Winding Form | Effective Date: | Date Performed: |
| --- | --- | --- |
| LIFT PROCEDURE NO.D -L-NCSX-983 AREA: NCSX Coil Manufacturing Facility | Repetitive Lift Expiration Date: | Approved: LIFT MANAGER |
| DISASSEMBLY PROCESS COMPLETED PIC: PROCEDURE PREREQUISITES COMPLETED QC: |
| DESCRIPTION: WEIGHT: 6200 Lbs. (max.) DETERMINED BY: Calculations Sketch of rigging shall include: Crane Capacity, Hook Load, All Rigging, Lift Height, Flight Plan Sketch of equipment shall include: Dimensions, Bolts Removed, Allowable Tilt |
| CRANE OPERATOR RIGGING TEAM (print) (print) APPROVED: QRS PIC LIFT ENGINEER (Rigged per sketch) (Equipment ready to lift) (Qualification/inspection complete) |

. . . PERFORM LIFT. . .  PERFORM LIFT . . . PERFORM LIFT . . .

Equipment is secure and rigging may be removed: PIC: Date Performed:

LIFT DATA SHEET AND ALL DATA TO BE RETURNED TO PPPL OPERATIONS CENTER.

# Text boxes

(2) Chain-falls
( 2-ton capacity each

1

1) Lift Coil

2) Extend chain-fall (1) to upend coil until slack and disconnect

3) Adjust chain-fall (2) to lift coil – disconnect two top long slings.

4) Reconnect chain-fall (1) on opposite side bottom.

5) Extend chain-fall (2) and or retract chain-fall (1) to level coil.

(8) slings various lengths vertical capacity ( 5,300 lbs. each [Green]

NOTE: Maximum Sling angle 45º

2

(8) Lift nut or Lift fixture plates, 
5/8” or ¾” swivel hoist ring, 
6 ½ ton shackle 
(as needed)

Connect slings to plate or nut on bottom of flange.

Coil No.

_____________