November 7, 2006

To: Fred Dahlgren, Mike Zarnstorff, Hutch Neilson

From: Wayne Reiersen

Subject: Eliminating PF6

Eliminating PF6 could potentially greatly simplify the coil structures.  A study was undertaken to assess the feasibility of this option.  The results do not look very promising.  Although PF1-5 could be used to provide the poloidal fields needed for the reference equilibria (see Figures 1-5), the PF currents were substantially higher (see Table 1).  Note that the poloidal fields for the reference equilibria were originally produced with PF3-6 alone.  The higher currents in PF1-5 would complicate rather than simplify the structural design (and analysis) of the stellarator core and make power supply upgrades more demanding which are not directions we want to go in.  The reduced coil set (PF2-5) is also less effective in reproducing the multipole fields compared to PF3-6 (see Figures 6-10).  The purpose of this memo is to just document that we turned over this rock.

Table 1 – Coil current (in amps) for reference equilibria

Figure 1

Figure 2

Figure 3

Figure 4

Figure 5

Figure 6

Figure 7

Figure 8

Figure 9

Figure 10

Cc: Strykowsky, Heitzenroeder, Williams, Nelson, Cole